Files-11 On-Disk Structure Specification


Andrew C. Goldstein
VAX/VMS Software Devlopment


11-Jan-1985


Copyright (c) 1985 Digital Equipment Corporation, Maynard, Mass.


The material included in this functional specification, including  but
not  limited  to  instruction  times  and  operating  speeds,  is  for
information purposes only.  All such material  is  subject  to  change
without  notice.   Consequently Digital Equipment Corporation makes no
claim and shall not be liable for its accuracy.


This software is furnished under a license for use only  on  a  single
computer system and may be copied only with the inclusion of the above
copyright notice.  This software, or any other copies thereof, may not
be provided or otherwise made available to any other person except for
use on such system and to one  who  agrees  to  these  license  terms.
Title  to  and  ownership of the software shall at all times remain in
Digital Equipment Corporation.


The information in this document is subject to change  without  notice
and  should  not  be  construed  as  a commitment by Digital Equipment
Corporation.


Digital Equipment Corporation assumes no responsibility for the use or
reliability  of  its  software  on  equipment which is not supplied by
Digital Equipment Corporation.



Specification Version:

Full Internal Specification

Files-11 On-Disk Structure                                      Page 2


Revision History:


15-Jan-1983     Andrew C.  Goldstein

                Corrections   resulting   from   VMS   implementation.
                Rearrange  reserved file ID's, remove free space file,
                remove proposed access control list and classification
                mask formats.

1-Oct-1983      Andrew C.  Goldstein

                Change all field names to VMS  structure  names.   Add
                disk  quotas,  access control lists, non-discretionary
                protection, and other  features  developed  since  VMS
                V1.5.  Add level 0 and level 1 subset descriptions.

11-Jan-1983     Andrew C.  Goldstein

                Changes to level 0 subset definition, based on review.

Files-11 On-Disk Structure                                      Page 3


1  Scope

This document is a specification of the  on-media  structure  that  is
used  by Files-11.  Files-11 is a general purpose file structure which
is intended to be the standard file structure for all medium to  large
PDP-11 and VAX systems.

This document describes structure level 2 of Files-11,  also  referred
to   as   ODS-2  (on-disk  structure  2).   It  contains  feature  and
reliability improvements over structure level 1 (ODS-1).



1.1  Conventions

All numerical values given in this  document  are  in  decimal  radix,
unless indicated otherwise.

Within the file structure are fields  containing  binary  integers  of
various  lengths.  Unless otherwise indicated, all these fields are in
the standard numerical format, which means that the  most  significant
bits are stored in the highest numbered address.

In the descriptions of various  structures  on  the  disk,  there  are
fields  that  are  labeled  "not used".  These fields must be zero, so
that they can be  made  non-zero  for  future  use.   Since  they  are
reserved  for future use, programs reading these structures should not
assume that these fields are in fact zero.



2  Medium

Files-11 is a structure which is imposed on  a  medium.   That  medium
must  have  certain  properties,  which are described in the following
section.  Generally speaking, block addressable storage  devices  such
as  disks  and  Dectape  are  suitable  for  Files-11;  hence Files-11
structured media are generically referred to as disks.



2.1  Volume

The basic medium that carries a Files-11 structure is referred to as a
______                                              _______ ______volume.   A  volume is defined as an ordered set of logical blocks.  A
logical block is an array of 512 8-bit bytes.  The logical blocks in a
volume  are  consecutively  numbered  from  0 to n-1, where the volume
contains n logical blocks.  The number assigned to a logical block  is
             _______  _____  ______       ___called  its  logical  block  number,  or  LBN.  Files-11 is capable of
describing volumes up to 2**32 blocks in size.  In practice, a  volume
should be at least 100 blocks in size to be useful.

The logical blocks of a volume  must  be  randomly  addressable.   The
volume  must  also  allow  transfers of any length up to 65K bytes, in
multiples of four bytes.  When a transfer is longer  than  512  bytes,

Files-11 On-Disk Structure                                      Page 4


consecutively  numbered  logical  blocks are transfered until the byte
count is satisfied.  In other words, the volume can  be  viewed  as  a
partitioned  array of bytes.  It must allow reads and writes of arrays
of any length up to 65K bytes, provided that they start on  a  logical
block  boundary and that the length is a multiple of four bytes.  When
only part of a block is written, the contents of the remainder of that
logical block will be undefined.

                                                ________The logical blocks of a volume are grouped into clusters.  The cluster
is  the  basic  unit  of space allocation on the volume.  Each cluster
contains one or more logical blocks; the number of blocks in a cluster
                ______ _______ ______     _______ ___ _______ ______is known as the volume cluster factor, or storage map cluster factor.

                                                    ____  _____A volume is identified as a Files-11 volume by the  home  block.   The
home  block  is  located at a defined physical location on the volume,
and is identified by the presence of checksums and predictable values.
The home block is described in detail in section 5.1.  To identify the
                                  ______ _____volume, the home block contains a volume label, which is a  string  of
up  to  12  ASCII  characters.   The  characters are restricted to the
printing ASCII set (i.e., excluding control  characters  and  rubout).
Further,  it  is  recommended  that  volume  labels  be  restricted to
alphanumerics only to avoid conflicts with the  command  languages  of
supporting systems.  The volume label of a volume may not be null.



2.2  Volume Sets

  ______ ___A volume set is a collection of  related  volumes  that  are  normally
treated  as  one logical device in the usual operating system concept.
Each volume contains its own Files-11 structure; however, files on the
                                                              ________various  volumes  in  a  volume  set may be referenced with a relative
______ ______volume number, which uniquely determines which volume in the  set  the
file is located on.

                                        _________  ____A volume set has associated with it  a  structure  name,  which  is  a
string  of  up to 12 ASCII characters which identifies the volume set.
The character set limitations of the volume label also  apply  to  the
structure name.  The structure name may not be null.



2.2.1  Tightly Coupled Volume Set

  _______ _______ ______ ___A tightly coupled volume set is a volume set which is  consistent  and
self  identifying.  The volume labels of the volumes making up the set
must be unique  within  the  set,  and  must  be  different  from  the
structure  name.  Relative volume one of the set contains a file which
lists  the  volume  labels  of  all  the  volumes  in  the  set,  thus
associating  volume  labels with relative volume numbers.  Each volume
is identified as being part of the set by carrying the structure name,
its volume label, and its relative volume number.

Files-11 On-Disk Structure                                      Page 5


2.2.2  Loosely Coupled Volume Set

  _______ _______ ______ ___A loosely coupled volume set is a collection of volumes which  is  not
self  identifying.   There is no file listing the volume labels.  Only
one file may cross from any one volume in  the  set  to  another,  and
files   in   the  set  which  cross  volumes  may  be  processed  only
sequentially.   Correct  sequencing  of  the  volumes  that   hold   a
particular  file  is the responsibility of the system operator and the
application using the volume set.  There are checks  that  will  catch
most  handling  errors,  but they cannot be foolproof.  The purpose of
the loosely coupled volume set is to emulate multi-volume magtape, and
allow  a  file to be read or written sequentially with only one volume
mounted at a time.



3  Files

Any data in a volume or volume set that is of any interest (i.e.,  all
                                                         ____blocks  not  available for allocation) is contained in a file.  A file
                     _______ ______is an ordered set of virtual blocks, where a virtual block is an array
of  512  8  bit bytes.  The virtual blocks of a file are consecutively
numbered from 1 to n, where n is the highest numbered block  that  has
been allocated to the file.  The number assigned to a virtual block is
                       _______ _____ ______     ___called (obviously) its virtual block number, or VBN.   Virtual  blocks
are  mapped  to  unique  logical blocks in the volume set by Files-11.
Virtual blocks may be processed in the same manner as logical  blocks.
Any  array  of  bytes  less than 65K in length may be read or written,
provided that the transfer starts on a virtual block boundary and that
its length is a multiple of four.

For most files, all VBN's less  than  or  equal  to  the  highest  VBN
allocated  map  to some LBN in the volume set.  Such files are said to
   _____                   ______be dense.  Files which are sparse contain virtual  blocks  which  have
not  been  allocated  logical  blocks.  Unallocated virtual blocks are
represented by mapping data containing an LBN of all ones (within  the
applicable  mapping  format).  [Sparsely allocated files have not been
implemented by any system supporting Files-11 so far.]



3.1  File ID

                                                      ____ __Each file in a volume set is uniquely identified by a File ID.  A File
ID  is  a  binary  value consisting of 48 bits.  It is supplied by the
file system when the file is created, and must be supplied by the user
whenever he wishes to reference a particular file.

A file ID is divided into the following  fields:   (In  this  and  all
subsequent structure illustrations, fields are shown 16 bits across.)


                |---------------------------------------|
                |              File Number              |  FID$W_NUM
                |---------------------------------------|

Files-11 On-Disk Structure                                      Page 6


                |          File Sequence Number         |  FID$W_SEQ
                |-------------------|-------------------|
FID$B_NMX       | File Number Ext.  | Rel. Vol. Number  |  FID$B_RVN
                |-------------------|-------------------|



3.1.1  FID$W_NUM - 2 Bytes Low Order File Number

          This word contains the low  16  bits  of  the  file  number.
          Taken together with FID$B_NMX, it forms a 24 bit file number
          that locates the file within  a  particular  volume  of  the
          volume  set.   The  set  of  file  numbers  on  a  volume is
          moderately (but not totally) dense; at any instant in time a
          file number uniquely identifies one file within that volume.
          File numbers for a volume start with 1 so that zero  is  not
          valid.   In  addition, file numbers with the low 16 bits all
          zero (i.e., multiples of 65536) are not  assigned  to  files
          for historical reasons.



3.1.2  FID$W_SEQ - 2 Bytes File Sequence Number

          Identifies the current use of an individual file number on a
          volume.   File  numbers  are re-used; when a file is deleted
          its file number becomes available for future  use  for  some
          other file.  Each time a file number is re-used, a different
          file sequence number is assigned to distinguish the uses  of
          that  file  number.   The  file sequence number is essential
          since it is  perfectly  legal  for  users  to  remember  and
          attempt  to  use  a  File  ID  long after that file has been
          deleted.  The preferred method for assigning  file  sequence
          numbers  is  to maintain the current sequence number in each
          file header  and  increment  it  each  time  the  header  is
          re-used.   A  file sequence numbers should only be generated
          randomly when the previous value of  the  header's  sequence
          number is unavailable.



3.1.3  FID$B_RVN - 1 Byte Relative Volume Number

          Identifies which volume of a volume set the file is  located
          on.   If  the volume in question is not a member of a volume
          set, then this word is zero.  If the volume  is  part  of  a
                                                          ___          volume set, then the relative volume number, or RVN, lies in
          the range from 1 to 255.  In any context where a  particular
          volume  of  a  volume  set can be identified as the "current
          volume", such as a file extension linkage, a relative volume
          number  of  zero means "the current volume".  When a file is
          referred to in the context of the volume on which  it  lies,
          it  should  be  referred to with a relative volume number of
          zero, regardless of the RVN that may  be  assigned  to  that
          volume.

Files-11 On-Disk Structure                                      Page 7


3.1.4  FID$B_NMX - 1 Byte File Number Extension

          This byte contains the high order part of the  file  number.
          Together  with  FID$W_NUM, it forms the complete 24 bit file
          number.

In this specification,  file  ID's  are  referred  to  in  the  format
"l,m,n",  where  l  is the file number, m is the file sequence number,
and n is the relative volume number.  If no relative volume number  is
given (i.e., a file ID of "l,m") it is assumed to be zero.



3.2  File Header

                                                   ____  ______Each file on a Files-11 volume is described by  a  file  header.   The
file  header is a block that contains all the information necessary to
access the file.  It is not part of the file; rather, it is  contained
in  the  volume's index file.  (The index file is described in section
5.1).  The header block is organized into  six  areas,  of  which  the
first five are variable in size.



3.2.1  Header Area

          The information in the header area permits the  file  system
          to  verify  that this block is in fact a file header and, in
          particular, is the header being  sought  by  the  user.   It
          contains  the  file  number  and file sequence number of the
          file, as well as its ownership and protection  codes.   This
          area  also  contains  offsets to the other areas of the file
          header, thus defining their size.



3.2.2  Ident Area

          The ident area of a file header contains identification  and
          accounting data about the file.  Stored here are the primary
          name of the file,  its  creation  date  and  time,  revision
          count,  date, and time, expiration date and time, and backup
          date and time.



3.2.3  Map Area

          The map area describes the mapping of virtual blocks of  the
          file  to the logical blocks of the volume.  The mapping data
                                _________  ________          consists of a list of retrieval  pointers.   Each  retrieval
          pointer   describes  one  group  of  consecutively  numbered
          logical blocks that are allocated to  the  file.   Retrieval
          pointers  are  arranged  in  the order of the virtual blocks
          they represent.

Files-11 On-Disk Structure                                      Page 8


3.2.4  Access Control List

          The access control list is an optional area that contains  a
          list  of  users  that  are  allowed access to the file.  The
          access control list  makes  it  possible  to  describe  user
          communities  for  a particular file that cannot be expressed
          with the regular protection  classes.   The  access  control
          list  area  may also be used to contain other ancillary file
          information of a variable nature.



3.2.5  Reserved Area

          This optional area is reserved for the use by CSS or special
          applications.   It  will  not  be  used by standard Files-11
          systems.



3.2.6  End Checksum

          The last two bytes of the  file  header  contain  a  16  bit
          additive  checksum  of  the  preceding 255 words of the file
          header.  The checksum is used to help verify that the  block
          is in fact a file header.



3.3  Multi-header Files

Since the file header is of fixed size, it is inevitable that for some
files  the  mapping  or access control information will not fit in the
allocated space.  A file with a large amount of such data is therefore
represented  with  a  chain  of  file  headers.   Each  header  maps a
consecutive set of virtual blocks; the extension linkage in the header
area  links  the  headers together in order of ascending virtual block
numbers.  The extension pointer in each file header is the File ID  of
the  next header in sequence.  The access control list segments in the
various headers are likewise considered one large access control list,
concatenated  in  the order of the file headers.  Access control lists
and arrays of map  pointers  may  be  arbitrarily  intermixed  in  the
various  headers of a file.  (i.e., each header may contain any amount
of map or access control  data  regardless  of  its  position  in  the
sequence.)

Each header of a multi-header file is technically accessible as a file
because  it  has  a  file  ID of its own.  However, since the complete
access control information is only visible from the primary header  of
a  file,  file  systems should restrict access to extension headers as
files to correctly enforce file protection.

Files-11 On-Disk Structure                                      Page 9


3.4  Multi-volume Files

Multiple headers are also needed for files  that  span  volumes  in  a
volume  set.   A  header  may  only  map logical blocks located on its
volume; therefore a multi-volume file is represented by headers on all
volumes  that  contain  portions of that file.  In a multi-volume file
contained on a loosely coupled volume set, the File ID  of  the  first
header on each continuation volume always has the value 7,7,n, where n
is the RVN of the volume on which the file starts plus the  number  of
preceding volumes containing portions of the file.



3.5  File Header - Detailed Description

This section describes in detail  the  items  contained  in  the  file
header.



3.5.1  Validity

A valid file header is defined by the following rules:

     1.  The header checksum in FH2$W_CHECKSUM is correct.

     2.  The contents of FH2$B_IDOFFSET is no  less  than  the  offset
         FH2$L_FILEOWNER/2.   [Due  to subsetting considerations, this
         value may be changed in the future.]

     3.  The  four  offset   bytes   are   related   in   the   manner
         (FH2$B_IDOFFSET)  <=  (FH2$B_MPOFFSET) <= (FH2$B_ACOFFSET) <=
         (FH2$B_RSOFFSET).

     4.  The high byte of FH2$W_STRUCLEV contains the value 2.

     5.  The low byte of FH2$W_STRUCLEV contains a  value  greater  or
         equal to 1.

     6.  The word FH2$W_FID_NUM contains the file number.

     7.  The word FH2$W_FID_SEQ contains the file sequence number.

     8.  The high byte FH2$W_FID_RVN contains the extended part of the
         file number, if any.

     9.  The contents of the byte FH2$B_MAP_INUSE must be less than or
         equal to (FH2$B_ACOFFSET) - (FH2$B_MPOFFSET).

Note that, since the header and ident areas are  variable  in  length,
software  processing  these  structures must check their length before
accessing any fields.  Fields contained within the minimum  length  of
the header area may, of course, be presumed present.

A deleted file header conforms to the format of a  valid  file  header

Files-11 On-Disk Structure                                     Page 10


with the following exceptions:

     1.  FH2$V_MARKDEL is set in FH2$L_FILECHAR.

     2.  FH2$W_FID_NUM, FH2$B_FID_NMX, and FH2$B_FID_RVN contain zero.

     3.  The file header checksum contains zero.




3.5.2  Header Area Description

The header area of the file  header  always  starts  at  byte  0.   It
contains  the  basic  information  needed for checking the validity of
accesses to the file.



3.5.2.1  FH2$B_IDOFFSET - 1 Byte        Ident Area Offset

          This byte contains the number of 16 bit  words  between  the
          start  of  the  file header and the start of the ident area.
          It defines the location of the ident area and  the  size  of
          the header area.



3.5.2.2  FH2$B_MPOFFSET - 1 Byte        Map Area Offset

          This byte contains the number of 16 bit  words  between  the
          start  of the file header and the start of the map area.  It
          defines the location of the  map  area  and,  together  with
          FH2$B_IDOFFSET, the size of the ident area.



3.5.2.3  FH2$B_ACOFFSET - 1 Byte        Access Control List Offset

          This byte contains the number of 16 bit  words  between  the
          start of the file header and the start of the access control
          list.  It defines the location of the ACL and, together with
          FH2$B_MPOFFSET, the size of the map area.



3.5.2.4  FH2$B_RSOFFSET - 1 Byte        Reserved Area Offset

          This byte contains the number of 16 bit  words  between  the
          start of the header and the start of the reserved area.  The
          reserved area will not be used by Files-11 itself,  and  may
          be  used  by  CSS  or  special  applications.  Together with
          FH2$B_ACOFFSET, this byte defines the  size  of  the  access
          control  list.   The size of the reserved area is implied by
          the contents of FH2$B_RSOFFSET and the  end  of  the  header

Files-11 On-Disk Structure                                     Page 11


          block.

          The presence of the ident, map, ACL, and reserved  areas  is
          optional.   Absence  of  any area is signalled not by a zero
          offset, but by the equality of the two offsets  that  define
          that  area's  size.   All five areas are variable in length;
          implementations of Files-11  must  check  the  length  of  a
          particular  area before attempting to reference a particular
          entry.



3.5.2.5  FH2$W_SEG_NUM - 2 Bytes        Extension Segment Number

          This word contains the value n, where  this  header  is  the
          n+1th  header  of  the  file;  i.e.,  headers  of a file are
          numbered sequentially starting with 0.



3.5.2.6  FH2$W_STRUCLEV - 2 Bytes       Structure Level and Version

          The file structure level and version  is  used  to  identify
          different  versions of Files-11 as they affect the structure
          of the file header.  This permits upwards  compatibility  of
          file  structures  as Files-11 evolves, in that the structure
          level word identifies the version of Files-11  that  created
          this  particular  file.   This  document describes structure
          level 2 of Files-11.  The high byte of  FH2$W_STRUCLEV  must
          contain  the  value  2.   The  low byte contains the version
          number, which must be greater or equal to  1.   The  version
          number will be incremented whenever compatible additions are
          made to the Files-11 structure that may be safely ignored by
          an  old version of the file system.  This document describes
          version 1 of structure level 2.



3.5.2.7  FH2$W_FID - 6 Bytes            File ID

          This field contains the file ID of the file, whose format is
          described  in  section  3.1  above.   The following subfield
          names exist:

          FH2$W_FID_NUM       low order file number
          FH2$W_FID_SEQ       file sequence number
          FH2$B_FID_RVN       relative volume number
          FH2$B_FID_NMX       high order file number

          Because the file ID refers to itself (and  therefore  always
          points to the same volume) FH2$B_FID_RVN is always zero.

Files-11 On-Disk Structure                                     Page 12


3.5.2.8  FH2$W_EXT_FID - 6 Bytes        Extension File ID

          This field contains the file ID of the file's next extension
          header, if one exists.  A contents of zero indicates that no
          extension header  exists.   The  format  of  a  file  ID  is
          discussed  in  section  3.1  above.   The following subfield
          names exist:

          FH2$W_EX_FIDNUM     low order file number
          FH2$W_EX_FIDSEQ     file sequence number
          FH2$B_EX_FIDRVN     relative volume number
          FH2$B_EX_FIDNMX     high order file number



3.5.2.9  FH2$W_RECATTR - 32 Bytes       File Record Attributes

          This area is used by the record manager, or any other higher
          level  access  mechanism, to store information necessary for
          processing the file, e.g., record control data, end of  file
          mark,  etc.  Certain portions of this area are controlled by
          this specification; see section 6 for details.



3.5.2.10  FH2$L_FILECHAR - 4 Bytes      File Characteristics

          The file characteristics field contains the  following  flag
          bits.  The bit names given are defined relative to the start
          of this field.

          FCH$V_NOBACKUP   Set if incremental backup is to be disabled
                           for this file.

          FCH$V_WRITEBACK  Set if the file may be  write-back  cached;
                           i.e., if a cache is used for the file data,
                           data written by a user is only written back
                           to  the  disk  when  is it removed from the
                           cache.   Clear  for   write-through   cache
                           operation.

          FCH$V_READCHECK  Set if the file is to be read-checked.  All
                           read  operations  on  the  file,  including
                           reads  of  the  file  header(s),  will   be
                           performed  with  a  read,  read-compare  to
                           assure data integrity.

          FCH$V_WRITCHECK  Set if the file  is  to  be  write-checked.
                           All write operations on the file, including
                           modifications of the file  header(s),  will
                           be  performed with a write, read-compare to
                           assure data integrity.

          FCH$V_CONTIGB    Set if the  file  is  allocated  contiguous
                           best   effort;   i.e.,   as  contiguous  as

Files-11 On-Disk Structure                                     Page 13


                           possible.

          FCH$V_LOCKED     Set if the file is  deaccess-locked.   This
                           bit is used as a flag warning that the file
                           was not properly  closed  and  may  contain
                           inconsistent  data.   Access to the file is
                           denied if this bit is set.

                                                _________  __________          FCH$V_CONTIG     Set if the file  is  logically  contiguous;
                           i.e.,  if  for  all  virtual  blocks in the
                           file, virtual block i maps to logical block
                           k+i  on  one  volume  for  some constant k.
                           This bit may be implicitly set  or  cleared
                           by  file  system  operations  that allocate
                           space to the file; the user may only  clear
                           it explicitly.

          FCH$V_BADACL     Set if the access control list of this file
                           is not valid (e.g., a system crash occurred
                           while it was being updated).

          FCH$V_SPOOL      Set if the  file  is  a  spool  file.   (An
                           intermediate file for later printing, etc.)
                           File operations not related to  spool  file
                           handling are prohibited.

          FCH$V_DIRECTORY  Set if the file is a directory.

          FCH$V_BADBLOCK   Set if there is a bad  data  block  in  the
                           file.  It indicates that deferred bad block
                           processing is to be done  on  the  file  at
                           some  suitable  later time (such as when it
                           is deleted.)

          FCH$V_MARKDEL    Set if the file is marked for  delete.   If
                           this  bit  is  set, further accesses to the
                           file are  denied,  and  the  file  will  be
                           physically   deleted   when  no  users  are
                           accessing it.

          FCH$V_NOCHARGE   Set if the space used by this file  is  not
                           to be charged to its owner.

          FCH$V_ERASE      Set  if  the   file   is   to   be   erased
                           (overwritten) when it is deleted.



3.5.2.11  FH2$W_RECPROT - 2 Bytes       Record Protection

          This field contains the record protection bits of the  file.
          [This  feature  has  never  been implemented, and this field
          will likely be used instead as a general  extension  of  the
          file protection mask FH2$W_FILEPROT described below.]

Files-11 On-Disk Structure                                     Page 14


3.5.2.12  FH2$B_MAP_INUSE - 1 Byte      Map Words in Use

          This byte contains a count of the number of map  area  words
          currently in use.



3.5.2.13  FH2$B_ACC_MODE - 1 Byte       Accessor Privilege Level

          This byte defines the lowest privilege  level  at  which  an
          accessor  must  be  running in order to be allowed access to
          the file.  Each privilege level is a two bit  integer;  zero
          refers  to  the  lowest  privilege  and  3  is  the highest.
          Privilege levels may be assigned  separately  to  the  basic
          file access modes, using the following bit assigment in this
          byte:

          Read      Bits 0 - 1
          Write     Bits 2 - 3
          Execute   Bits 4 - 5
          Delete    Bits 6 - 7

          An operating system should map its  privilege  level  coding
          onto  this  code  in  the  smoothest  manner  possible.  For
          example, the four access modes  of  VMS,  user,  supervisor,
          exec, and kernel, are coded as 0 through 3, respectively.  A
          system such as RSX-11M which has only two levels (privileged
          and  non-privileged),  should  map  the  two  onto  3 and 0,
          respectively.

          Privilege levels are meant to confine access to the contents
          of  files  to suitably trustworthy procedures.  Thus, a user
          might be denied the ability to  write  a  record  structured
          file  directly  (on  a  virtual  block  basis), but would be
          permitted to write the  file  through  the  record  manager,
          which would be suitably privileged.

          For  a  record  structured  file,  an  appropriate  set   of
          privilege  levels  would  be 0,2,0,0, expressed in the order
          read - write - execute - delete.



3.5.2.14  FH2$L_FILEOWNER - 4 Bytes     File Owner UIC

          These words contain  the  binary  user  identification  code
          (UIC)  of  the owner of the file.  The file owner is usually
          (but not necessarily) the creator of the file.



3.5.2.15  FH2$W_FILEPROT - 2 Bytes      File Protection Code

          This word controls what access all users in the  system  may
          have  to  the  file.   Accessors  of  a file are categorized

Files-11 On-Disk Structure                                     Page 15


          according  to  the  relationship  between  the  UIC  of  the
          accessor  and  the  UIC  of  the  owner  of  the file.  Each
          category is controlled by a four bit field in the protection
          word.  The category of the accessor is selected as follows:

          System    Bits 0 - 3

                    The accessor is subject to  system  protection  if
                    the  project  number  of the UIC under which he is
                    running is 10  octal  or  less,  or  is  otherwise
                    deemed  a  "system" process (e.g., in VMS, holding
                    SYSPRV privilege).

          Owner     Bits 4 - 7

                    The accessor is subject to owner protection if the
                    UIC  under which he is running exactly matches the
                    file owner UIC.

          Group     Bits 8 - 11

                    The accessor is subject to group protection if the
                    project  number  of  his  UIC  matches the project
                    number of the file owner UIC.

          World     Bits 12 - 17

                    The accessor is subject to world protection if  he
                    does not fit into any of the above categories.

          Four types of access are defined in Files-11:  read,  write,
          execute,  and delete.  Each four bit field in the protection
          word is bit encoded to permit or deny any combination of the
          four types of access to that category of accessors.  Setting
          a bit denies that type of access to that category.  The bits
          within each four bit field are used as follows:

          Bit 0     Set to deny read access
          Bit 1     Set to deny write access
          Bit 2     Set to deny execute access
          Bit 3     Set to deny delete access

          When a user attempts to access a file, protection checks are
          performed  in all the categories to which he is eligible, in
          the order system - owner -  group  -  world.   The  user  is
          granted access to the file if any of the categories to which
          he is eligible grants him access.

          A fifth type of access,  called  "control"  access,  governs
          changing  the  attributes of a file, such as its protection,
          characteristics, etc.  Control access is not  granted  by  a
          protection  mask,  but  is  always  available  to system and
          owner, and never to group and world.

          Recommended defaults for file protection for an "open  shop"

Files-11 On-Disk Structure                                     Page 16


          system  are [RWD,RWD,RW,R] (expressed in the order of system
          - owner - group -  world,  where  each  letter  denotes  the
          presence of that permission).  Observe that only files which
          contain executable programs should have  execute  protection
          turned  on.  Recommended defaults for a "closed shop" system
          are [RWD,RWD,R,].



3.5.2.16  FH2$W_BACKLINK - 6 Bytes      Back Link File ID

          This field  contains  the  file's  back  link  pointer.   It
          contains the file ID of the directory file that contains the
          primary directory entry for the file.  If the file header is
          an  extension  header, the back link contains the file ID of
          the primary header, if  one  exists.   A  contents  of  zero
          indicates that no back link exists.  The format of a file ID
          is discussed in section 3.1 above.  The  following  subfield
          names exist:

          FH2$W_BK_FIDNUM     low order file number
          FH2$W_BK_FIDSEQ     file sequence number
          FH2$B_BK_FIDRVN     relative volume number
          FH2$B_BK_FIDNMX     high order file number



3.5.2.17  FH2$W_JOURNAL - 2 Bytes       Journal Control Flags

          This field contains flags used to  control  the  journalling
          facility  provided  by  a  higher  level access method.  The
          following flag bits are defined (relative to  the  start  of
          this field):

          FJN$V_RUACCESS   Set if the file is permitted to be accessed
                           only  if  the  accessor  is running under a
                           recovery unit.

          FJN$V_RUJNL      Set if a recovery unit  journal  is  to  be
                           enabled

          FJN$V_BIJNL      Set if a before  image  journal  is  to  be
                           enabled

          FJN$V_AIJNL      Set if an after  image  journal  is  to  be
                           enabled

          FJN$V_ATJNL      Set if an audit  trail  journal  is  to  be
                           enabled

          FJN$V_NORU       Set if the file is not to be accessed  from
                           within a recovery unit

Files-11 On-Disk Structure                                     Page 17


3.5.2.18  2 Bytes (not used)

3.5.2.19  FH2$L_HIGHWATER - 4 Bytes     File Highwater Mark

          This field contains the highest virtual block plus 1 of  the
          file that has been written (i.e., the first VBN that has not
          been written).  File systems enforcing  security  protection
          should prevent the reading of blocks past this point.

          If the contents of the highwater mark field is zero  (or  if
          the header area is too short to contain this field), then no
          highwater mark has been maintained for the  file.   In  this
          case,  the  file  system  should  waive  enforcement  of the
          highwater mark.



3.5.2.20  FH2$C_LENGTH - 80 Bytes       Size of Default Header Area

          This symbol represents the total size  of  the  header  area
          containing all of the above entries.



3.5.2.21  8 Bytes                       (not used)

3.5.2.22  FH2$R_CLASS_PROT - 20 Bytes   Security Classification Mask

          This field contains the security classification of the file,
          to  be used when the file system enforces a Bell & La Padula
          lattice model  security  system.   The  classification  mask
          block has the following structure (the field names given are
          defined relative to the start  of  the  classification  mask
          block.)


                |-------------------|-------------------|
CLS$B_INTEG_LEV |  Integrity Level  |  Security Level   |  CLS$B_SECUR_LEV
                |-------------------|-------------------|
                |               (Not used)              |
                |---------------------------------------|
                |                                       |  CLS$Q_SECUR_CAT
                |--                                   --|
                |               Security                |
                |--             Category              --|
                |                 Mask                  |
                |--                                   --|
                |                                       |
                |---------------------------------------|
                |                                       |  CLS$Q_INTEG_CAT
                |--                                   --|
                |               Integrity               |
                |--             Category              --|
                |                 Mask                  |
                |--                                   --|

Files-11 On-Disk Structure                                     Page 18


                |                                       |
                |---------------------------------------|


          CLS$B_SECUR_LEV  Security level.   This  byte  contains  the
                           security classification level, encoded as 0
                           meaning the least  sensitive  and  255  the
                           most sensitive.

          CLS$B_INTEG_LEV  Integrity level.  This  byte  contains  the
                           integrity  classification level, encoded as
                           0 meaning the least trustworthy and 255 the
                           most trustworthy.

                           2 bytes - not used.

          CLS$Q_SECUR_CAT  This 8 byte field contains a bitmask of the
                           security      information      compartments
                           applicable to the file.

          CLS$Q_INTEG_CAT  This 8 byte field contains a bitmask of the
                           integrity      information     compartments
                           applicable to the file.



3.5.3  Ident Area Description


The ident area of the file header begins  at  the  word  indicated  by
FH2$B_IDOFFSET.   It contains identification and accounting data about
the file.  To allow more room for map pointers and access control list
entries, the ident area is customarily truncated in extension headers.



3.5.3.1  FI2$T_FILENAME - 20 Bytes      File Name

          This area contains the name of the file  in  ASCII.   A  dot
          separates  name  from  type,  and a semicolon separates type
          from version; both are  always  present.   If  the  name  is
          shorter  than  20  bytes, it is padded with blanks; if it is
          longer, it is continued in the FI2$T_FILENAMEXT field below.



3.5.3.2  FI2$W_REVISION - 2 Bytes       Revision Number

          This word contains the revision count of the file in binary.
          The  revision count is the number of times the file has been
          accessed for write.

Files-11 On-Disk Structure                                     Page 19


3.5.3.3  FI2$Q_CREDATE - 8 Bytes        Creation Date and Time

          These eight bytes contain the date and  time  at  which  the
          file  was  created.   The  time is expressed in the standard
          internal time format, which is a 64 bit integer representing
          tenths  of  microseconds elapsed since midnight, 17 November
          1858.



3.5.3.4  FI2$Q_REVDATE - 8 Bytes        Revision Date and Time

          The revision time is the time at which  the  file  was  last
          deaccessed  after being accessed for write.  It is expressed
          as the same format as the creation time above.



3.5.3.5  FI2$Q_EXPDATE - 8 Bytes        Expiration Date and Time

          These eight bytes contain the date and  time  at  which  the
          file becomes eligible to be deleted.  The format is the same
          as that of the creation and revision times above.



3.5.3.6  FI2$Q_BAKDATE - 8 Bytes        Backup Date and Time

          These eight bytes contain the date and  time  at  which  the
          file  was  last  backed  up.   The format is the same as the
          other dates and times.



3.5.3.7  FI2$T_FILENAMEXT - 66 Bytes    File Name Extension

          This  field  contains  the  remainder  of  the  file   name,
          continued from the FI2$T_FILENAME field above.  The total 86
          character file name field allows for 80 characters  of  name
          and type, plus a 5 digit version number.



3.5.3.8  FI2$C_LENGTH - 120 Bytes       Size of Ident Area

          This symbol represents the size of the ident area containing
          all of the above entries.



3.5.4  Map Area Description


The map area of the file  header  starts  at  the  word  indicated  by
FH2$B_MPOFFSET.   It  contains  the  information  necessary to map the

Files-11 On-Disk Structure                                     Page 20


virtual blocks of the file to the logical blocks of the volume.   This
area  contains  the  retrieval  pointers that actually map the virtual
blocks of the  file  to  the  logical  blocks  of  the  volume.   Each
                                ______retrieval  pointer describes an extent, a consecutively numbered group
of logical blocks which is allocated to the  file.   The  count  field
contains  the  binary  value  n  to  represent  a group of n+1 logical
blocks.  The logical block number field  contains  the  logical  block
number  of  the first logical block in the group.  Thus each retrieval
pointer maps virtual blocks  j  through  j+n  into  logical  blocks  k
through  k+n,  respectively,  where  j is the total number plus one of
virtual blocks represented by all preceding retrieval pointers in this
and all preceding headers of the file, n is the value contained in the
count field, and k is the value contained in the logical block  number
field.  Observe that j, k, and n+1 must always be integer multiples of
v, the volume cluster factor.

If the LBN field of a  retrieval  pointer  contains  all  ones  (i.e.,
points  to  block  2**22-1  or  2**32-1),  then that retrieval pointer
represents an unallocated portion of a sparse file.  The  count  field
describes  the  number  of  unallocated  virtual  blocks in the normal
manner.

There are four formats of retrieval  pointers,  identified  by  escape
codes.   The different formats may be intermixed within a file header.
The format code of each retrieval pointer is contained in the two high
order bits of the first word; this field is named FM2$V_FORMAT.




3.5.4.1  FM2$C_PLACEMENT = Format 0 - two bytes


                |----|----------------------------------|
FM2$V_FORMAT    | 00 |     Placement Control Flags      |  FM2$W_WORD0
                |----|----------------------------------|


          Retrieval pointer format 0 is used to store  placement  data
          in  the  file  header.   It  describes the placement control
          supplied with the  allocation  that  created  the  following
          retrieval  pointer,  allowing  the placement of a file to be
          replicated  when  the  file  is  copied  or  backed  up  and
          restored.   The  following  flag  bits  exist in a placement
          pointer:

          FM2$V_EXACT      Set if exact placement was requested (i.e.,
                           the allocation must be done as specified)

          FM2$V_ONCYL      Set if the allocation was to be located  on
                           one cylinder of the volume

          FM2$V_LBN        Set if the allocation was to be located  at
                           the starting LBN contained in the following
                           retrieval pointer

Files-11 On-Disk Structure                                     Page 21


          FM2$V_RVN        Set if the allocation was to be located  on
                           the  specified  volume (i.e., the volume on
                           which this extent is located)



3.5.4.2  FM2$C_FORMAT1 = Format 1 - four bytes.


                |----|--------------|-------------------|
FM2$V_FORMAT    | 01 |   High LBN   |    Block Count    |  FM2$B_COUNT1
FM2$V_HIGHLBN   |----|--------------|-------------------|
                |             Low Order LBN             |  FM2$W_LOWLBN
                |---------------------------------------|


          Retrieval pointer format 1 provides an 8 bit count field and
          a 22 bit LBN field.  It is therefore capable of representing
          a group of up to 256 blocks on a volume up to  2**22  blocks
          in size.



3.5.4.3  FM2$C_FORMAT2 = Format 2 - six bytes.


                |----|----------------------------------|
FM2$V_FORMAT    | 10 |           Block Count            |  FM2$V_COUNT2
                |----|----------------------------------|
                |                                       |  FM2$L_LBN2
                |--                LBN                --|
                |                                       |
                |---------------------------------------|


          Retrieval pointer format 2 provides a 14 bit count field and
          a  32  bit LBN field.  It is capable of representing a group
          of up to 16384 blocks on a volume  up  to  2**32  blocks  in
          size.



3.5.4.4  FM2$C_FORMAT3 = Format 3 - eight bytes.


                |----|----------------------------------|
FM2$V_FORMAT    | 11 |      High Order Block Count      |  FM2$V_COUNT2
                |----|----------------------------------|
                |         Low Order Block Count         |  FM2$W_LOWCOUNT
                |---------------------------------------|
                |                                       |  FM2$L_LBN3
                |--                LBN                --|
                |                                       |
                |---------------------------------------|

Files-11 On-Disk Structure                                     Page 22


          Retrieval pointer format 3 provides a 30 bit count field and
          a  32 bit LBN field.  It is capable of describing a group of
          up to 2**30 blocks on a volume up to 2**32 blocks in size.





3.5.5  Access Control List

(Reserved for future use by DEC).



3.5.6  Reserved Area


The reserved area of the file header starts at the word  indicated  by
the  byte  FH2$B_RSOFFSET.  This area is not used by standard Files-11
file  managers,  but  is  available  for  use  by  CSS   and   special
applications.



3.5.7  End Checksum Description


The header checksum occupies the last two bytes of  the  file  header.
It  is  verified  every time a header is read, and is recomputed every
time a header is written.



3.5.7.1  FH2$W_CHECKSUM - 2 Bytes       Block Checksum


          This word is a simple additive checksum of all  other  words
          in  the  block.   It  is  computed  by  the following PDP-11
          routine or its equivalent:

                  MOV     Header-address,R0
                  CLR     R1
                  MOV     #255.,R2
          10$:    ADD     (R0)+,R1
                  SOB     R2,10$
                  MOV     R1,(R0)



3.6  File Header Layout

The following is a graphical layout of the fields in the file header.

Files-11 On-Disk Structure                                     Page 23


Header Area

                |-------------------|-------------------|
FH2$B_MPOFFSET  |  Map Area Offset  | Ident Area Offset |   FH2$B_IDOFFSET
                |-------------------|-------------------|
FH2$B_RSOFFSET  | Resv. Area Offset |  ACL Area Offset  |   FH2$B_ACOFFSET
                |-------------------|-------------------|
                |          File Segment Number          |   FH2$W_SEG_NUM
                |---------------------------------------|
                |         File Structure Level          |   FH2$W_STRUCLEV
                |---------------------------------------|   FH2$W_FID
                |                                       |   FH2$W_FID_NUM
                |--                                   --|
                |                File ID                |   FH2$W_FID_SEQ
                |--                                   --|
FH2$B_FID_NMX   |                                       |   FH2$B_FID_RVN
                |---------------------------------------|   FH2$W_EXT_FID
                |                                       |   FH2$W_EX_FIDNUM
                |--                                   --|
                |           Extension File ID           |   FH2$W_EX_FIDSEQ
                |--                                   --|
FH2$B_EX_FIDNMX |                                       |   FH2$B_EX_FIDRVN
                |---------------------------------------|
                |                                       |   FH2$W_RECATTR
                |                                       |
                |                                       |
                |         Record Attributes Area        |    
                |                                       |
                |                                       |
                |                                       |
                |---------------------------------------|
                |                                       |   FH2$L_FILECHAR
                |--        File Characteristics       --|
                |                                       |
                |---------------------------------------|
                |            Record Protection          |   FH2$W_RECPROT
                |-------------------|-------------------|
FH2$B_ACC_MODE  |    Access Level   | Map Words in Use  |   FH2$B_MAP_INUSE
                |-------------------|-------------------|
                |                                       |   FH2$L_FILEOWNER
                |--          File Owner UIC           --|
                |                                       |
                |---------------------------------------|
                |            File Protection            |   FH2$W_FILEPROT
                |---------------------------------------|   FH2$W_BACKLINK
                |                                       |   FH2$W_BK_FIDNUM
                |--                                   --|
                |         File Header Back Link         |   FH2$W_BK_FIDSEQ
                |--                                   --|
FH2$B_BK_FIDNMX |                                       |   FH2$B_BK_FIDRVN
                |---------------------------------------|
                |         Journal Control Flags         |   FH2$W_JOURNAL
                |---------------------------------------|
                |              (not used)               |
                |---------------------------------------|

Files-11 On-Disk Structure                                     Page 24


                |                                       |   FH2$L_HIGHWATER
                |--        File Highwater Mark        --|
                |                                       |
                |---------------------------------------|   FH2$C_LENGTH
                |                                       |
                |--                                   --|
                |                                       |
                |--            (not used)             --|
                |                                       |
                |--                                   --|
                |                                       |
                |---------------------------------------|
                |                                       |   FH2$R_CLASS_PROT
                |--                                   --|
                |                                       |
                |--                                   --|
                |      Security Classification Mask     |
                |--                                   --|
                |                                       |
                |--                                   --|
                |                                       |
                |---------------------------------------|


Ident Area

                |---------------------------------------|
                |                                       |   FI2$T_FILENAME
                |--                                   --|
                |                                       |
                |--                                   --|
                |               File Name               |    
                |--                                   --|
                |                                       |
                |--                                   --|
                |                                       |
                |---------------------------------------|
                |            Revision Number            |   FI2$W_REVISION
                |---------------------------------------|
                |                                       |   FI2$Q_CREDATE
                |--                                   --|
                |                                       |
                |--           Creation Date           --|
                |                                       |
                |--                                   --|
                |                                       |
                |---------------------------------------|
                |                                       |   FI2$Q_REVDATE
                |--                                   --|
                |                                       |
                |--           Revision Date           --|
                |                                       |
                |--                                   --|
                |                                       |
                |---------------------------------------|

Files-11 On-Disk Structure                                     Page 25


                |                                       |   FI2$Q_EXPDATE
                |--                                   --|
                |                                       |
                |--          Expiration Date          --|
                |                                       |
                |--                                   --|
                |                                       |
                |---------------------------------------|   
                |                                       |   FI2$Q_BAKDATE
                |--                                   --|
                |                                       |
                |--            Backup Date            --|
                |                                       |
                |--                                   --|
                |                                       |
                |---------------------------------------|
                |                                       |   FI2$T_FILENAMEXT
                |                                       |
                |                                       |
                |          File Name Extension          |
                |                                       |
                |                                       |
                |                                       |
                |---------------------------------------|   FI2$C_LENGTH



Map, ACL, and Reserved Areas

                |---------------------------------------|
                |                                       |
                |                                       |
                |                                       |
                |          Retrieval Pointers           |    
                |                                       |
                |                                       |
                |                                       |
                |---------------------------------------|
                |                                       |
                |                                       |
                |                                       |
                |          Access control List          |    
                |                                       |
                |                                       |
                |                                       |
                |---------------------------------------|
                |                                       |
                |                                       |
                |                                       |
                |             Reserved Area             |   
                |                                       |
                |                                       |
                |                                       |
                |---------------------------------------|
                |         File Header Checksum          |   FH2$W_CHECKSUM

Files-11 On-Disk Structure                                     Page 26


                |---------------------------------------|



4  Directories

Files-11 provides directories to allow the organization of files in  a
meaningful  way.   While  the  File  ID is sufficient to locate a file
uniquely on a volume set, it  is  hardly  mnemonic.   Directories  are
files whose function is to associate alphabetic names with File ID's.



4.1  Directory Heirarchies

Since directories are files with no  special  attributes,  directories
may  list  files  that  are  in  turn  directories.  Thus the user may
construct directory heirarchies of arbitrary depth and  complexity  to
structure his files as he pleases.



4.1.1  Two Level Directory Heirarchy


Implementations of Files-11 on existing PDP-11 systems all  support  a
two  level  directory  heirarchy  which  is  tied  in  with  the  user
identification mechanism of the operating system.  Each UIC  known  to
                                ____ ____ _________the system is associated with a user file directory (UFD).  References
to files that do not specify a directory are  generally  defaulted  to
the  UFD  associated with the user's UIC.  The syntax used to refer to
UIC's is the same as that used to identify the  directory  in  a  file
name  string.   The construct "[n,m]" is used to refer to group number
n, member number m.  All UFD's are listed in the volume's master  file
directory  (MFD)  under  a  file  name  constructed from the directory
string.  (See section 5.0 for a description of the MFD.) A  string  of
"[n,m]"  associates with a directory name of "nnnmmm.DIR;1", where nnn
and mmm are n and m padded out  to  three  digits  each  with  leading
zeroes.  Note that all number conversions are done in octal.

Two points should be noted here.  The UFD structure described here  is
not  intrinsically  part of the Files-11 on-disk structure; rather, it
is  a  convenient  cataloging  system  applied  by  various  operating
systems.   Also,  there  is  no hard and fast relationship between the
owner UIC of a file and the UFD in which  it  is  listed.   Generally,
they will correspond, but not necessarily.



4.1.2  Multi-level Directory Heirarchy


Contemporary implementations of Files-11 such as VMS use a multi-level
directory  heirarchy,  where the first level below the MFD is referred
to as the user file directory (UFD) and subsequent levels are referred

Files-11 On-Disk Structure                                     Page 27


to  as  sub  file  directories  (SFD's).   The  top level directory is
typically  used  to  represent  individual  system  users,  or   major
facilities,  etc.  Thus MFD entries would correspond to the user names
in  a  multi-user  system.   A  directory  specifier  has  the  format
"[name1.name2.name3. ... ]".   Each  name  in the list translates to a
directory file name of the form "name.DIR;1" and is  searched  for  in
the current directory level.

Observe that the directory protocol is not tied to the structure level
of  the disk.  Thus new systems will always have to handle the "[n,m]"
construct, which maps to a UFD name  of  "nnnmmm.DIR;1"  and  provides
only  two levels of directory.  Old systems will not be able to handle
volumes written with a multi-level directory structure.



4.1.3  Multi-Volume Directory Structure

In a volume set, the MFD for the all of the user files on  the  volume
set  is  the MFD of relative volume 1.  Its entries can point to UFD's
located on any volume in the set, whose entries can in turn  point  to
files  and sub directories on any volume in the set.  The MFD's of the
remaining volumes in the set only list  the  reserved  files  on  each
volume.

The assignment of volumes to specific directories  and  files  is  not
covered  by  this  specification.   Different  systems  may  implement
different  policies  to  trade  off  factors  such   as   performance,
reliability,   and  separability.   Optimizing  for  performance,  for
example, usually means scattering the files as  randomly  as  possible
across  the  volume set to make the most use of the available multiple
positioners.  Maximum separability (the ability to make  use  of  only
part  of  the  volume  set)  is achieved by locating files on the same
volume as their directories, and possibly entering the directories  in
the MFD's of the volumes on which they reside.



4.2  Directory Structure

A  directory  is  a  contiguous  file  which  has  the  directory  bit
(FCH$V_DIRECTORY)  set  in  its file characteristics (FH2$L_FILECHAR).
It is organized as a sequential file  with  variable  length  records,
with  the  attribute  set  that  records do not cross block boundaries
(FAT$V_NOSPAN), and no carriage control attributes.  The last word  of
the  directory  file's record attributes area (FAT$W_VERSIONS) is used
to store the directory's default version limit.  This version limit is
assigned  to all new files created in the directory if a version limit
is not specified by the creator.

Directory records within each block are packed together to conform  to
the  variable  length  record  format.   At the end of the sequence of
records in each block, a word of -1 signals the  end  of  records  for
that  block.  (See section 6 for a discussion of record formats.) Note
that in a directory block, the -1 word is always present,  whereas  in

Files-11 On-Disk Structure                                     Page 28


the variable length record format its presence is optional.

The entries in a directory are sorted alphabetically,  permitting  the
use  of  an  optimized search.  Entries which are multiple versions of
the same name and type are arranged in  order  of  decreasing  version
number  to optimize version related operations.  Each directory record
consists of the following:


                |---------------------------------------|
                |           Record Byte Count           |   DIR$W_SIZE
                |---------------------------------------|
                |             Version Limit             |   DIR$W_VERLIMIT
                |-------------------|-------------------|
DIR$B_NAMECOUNT |  Name Byte Count  |       Flags       |   DIR$B_FLAGS
                |-------------------|-------------------|
                |                                       |   DIR$T_NAME
                |                                       |
                |                                       |
                |           File Name String            |
                |                                       |
                |                                       |
                |                                       |
                |---------------------------------------|
                |                                       |
                |                                       |
                |              Value Field              |
                |                                       |
                |                                       |
                |---------------------------------------|



4.2.1  DIR$W_SIZE - 2 Bytes   Record Byte Count

          This field is the standard byte count field  of  a  variable
          length  record.   It  contains  the  length  in bytes of the
          record (not including the two bytes of the count).  The byte
          count is always even.



4.2.2  DIR$W_VERLIMIT - 2 Bytes         File Version Limit

          This word contains the maximum number of versions  that  are
          to  be retained for this name and type.  An attempt to enter
          more versions than the limit will result in the deletion  of
          the  least  recent  version,  or  an  error  return,  at the
          implementing system's option.

Files-11 On-Disk Structure                                     Page 29


4.2.3  DIR$B_FLAGS - 1 Byte   Flags

          This byte contains the type code of the directory entry  and
          assorted flag bits.  It contains the following subfields and
          status bits:

          DIR$V_TYPE       The type code is contained in the three low
                           bits  of  the flags byte.  It is one of the
                           following values:

          DIR$C_FID        The  value  field  is  a  list  of  version
                           numbers and 48 bit File Id's.

          DIR$C_LINKNAME   The value field is a symbolic  link  string
                           (i.e.,  an  alphabetic file specification).
                           [Symbolic links are not  yet  supported  by
                           any implementation of Files-11.]

                           [No status bits are defined at present.]



4.2.4  DIR$B_NAMECOUNT - 1 Byte         File Name Length

          This field contains the length in bytes of the file name.



4.2.5  DIR$T_NAME - Variable            File Name String

          This field  contains  the  file  name  and  type  in  ASCII,
          separated  by  a  a  dot.  The dot is present even if either
          name, or type, or both, are  null.   Only  name  constituent
          characters  may  be  present  in  the  name  and type.  Name
          constituent  characters  include  alphanumerics   (including
          supported foreign language characters), $, _, and -.  If the
          length of the name is odd, the name string is padded with  a
          single null.  [Note:  At present, the collating sequence for
          foreign language alphabetics has not yet been defined.  This
          will  occur in the near future when the first implementation
          is done.]



4.2.6  Value Field - Variable

          This field contains the  "value"  of  the  directory  entry;
          i.e.,  the  information  returned  to the user from a lookup
          operation.  If the directory record is a File ID  list  (the
          type  field  is  DIR$C_FID),  the  value  field is a list of
          version numbers and corresponding file  ID's,  appearing  in
          descending  order  by version number.  The number of entries
          in the list is deduced from the record byte count.

Files-11 On-Disk Structure                                     Page 30


                |---------------------------------------|
                |            Version Number             |   DIR$W_VERSION
                |---------------------------------------|   DIR$W_FID
                |                                       |   DIR$W_FID_NUM
                |--                                   --|
                |                File ID                |   DIR$W_FID_SEQ
                |--                                   --|
DIR$B_FID_NMX   |                                       |   DIR$B_FID_RVN
                |---------------------------------------|
                |            Version Number             |
                |---------------------------------------|
                |                                       |
                |--                                   --|
                |                File ID                |
                |--                                   --|
                |                                       |
                |---------------------------------------|
                |                                       |
                                    :
                                    :
                                    :
                                    :
                                    :
                |                                       |
                |---------------------------------------|
                |            Version Number             |
                |---------------------------------------|
                |                                       |
                |--                                   --|
                |                File ID                |
                |--                                   --|
                |                                       |
                |---------------------------------------|



4.2.7  DIR$W_VERSION - 2 Bytes          Version Number

          This word contains the version number of the directory entry
          in  binary.  Version numbers must lie in the range from 1 to
          32767.



4.2.8  DIR$W_FID - 6 Bytes              File ID

          These three words are the file ID that the  directory  entry
          points to.



4.3  Multiple Directory Records

Since directory records may not cross block  boundaries,  there  is  a
limit  to  the  number of file versions that may be represented in one

Files-11 On-Disk Structure                                     Page 31


directory record.  (That number is 62 for the shortest  possible  file
name.)  To  represent  more  versions of a file than will fit into one
directory block, multiple directory records are used.  The records are
ordered  by descending version number, as are the versions within each
record.  Each record contains the full file name.



5  Reserved Files

Clearly any file system must  maintain  some  data  structure  on  the
medium  which  is  used to control the file organization.  In Files-11
this data is kept in several files.  These files are  created  when  a
new  volume  is  initialized.  They are unique in that their File ID's
are known constants.  Note, however, that the relative  volume  number
used  when accessing one of these files depends upon the context.  The
exact number of these files which is present on  a  particular  volume
may  vary; however, at least five must be present.  All of these files
are non-deletable.  These files have the following uses:

                   _____ ____File ID 1,1 is the index file.  The index file  is  the  root  of  the
entire  Files-11  structure.  It contains the volume's bootstrap block
and the home block, which is used to identify the  volume  and  locate
the  rest  of the file structure.  The index file also contains all of
the file  headers  for  the  volume,  and  a  bitmap  to  control  the
allocation of file headers.

                   _______ ______ ____File ID 2,2 is the storage bitmap file.  It is  used  to  control  the
allocation of logical blocks on the volume.

                   ___ _____ ____File ID 3,3 is the bad block file.  It is a file containing all of the
known bad blocks on the volume.

                          ______ ____ _________      ___File ID 4,4 is the volume master file directory (or  MFD).   It  forms
the  root of the volume's directory structure.  The MFD lists the five
known files, all first level  user  directories,  and  whatever  other
files the user chooses to enter.

                          ____  _____  ____File ID 5,5 is the system core  image  file.   Its  use  is  operating
system dependent; its basic purpose is to provide a file of known File
ID for the use of the operating system.

                   ______ ___ ____ ____File ID 6,6 is the volume set list file.  If this volume  is  relative
volume  one of a tightly coupled volume set, this file contains a list
of the labels of all the volumes in the set.

                   ________ ____________ ____File ID 7,7 is the standard continuation file.  If this volume is part
of  a loosely coupled volume set, this file contains the first segment
of the portion of the multi-volume file that resides on this volume.

                   ______ _______ ____File ID 8,8 is the backup journal file.  This file is used to log  and
control the use of an incremental backup system.

                   _______ ___ _____ ___ ____File ID 9,9 is the pending bad block log file.  This file  contains  a
list  of  suspected  bad  blocks  on the volume that have not yet been

Files-11 On-Disk Structure                                     Page 32


turned over to the bad block file.

More File ID's may be reserved in the future; users  should  not  make
any assumptions about the values of user created File ID's.



5.1  Index File

The index  file  is  File  ID  1,1.   It  is  listed  in  the  MFD  as
INDEXF.SYS;1.  The index file is the root of the Files-11 structure in
that it provides the means for identification and initial access to  a
Files-11  volume,  and  contains  the access data for all files on the
volume (including itself).  This file has the  record  format  of  512
byte  fixed  length records, with no carriage control.  (See section 6
for a description of the sequential file format.)



5.1.1  Bootstrap Block


                                                  ____ _____Virtual block 1 of the index file is the volume's boot block.   It  is
almost  always mapped to logical block 0 of the volume.  If the volume
is the system device of an operating system, the boot  block  contains
an operating system dependent program which reads the operating system
into memory when the boot block is read and executed  by  a  machine's
hardware  bootstrap.   If  the volume is not a system device, the boot
block contains a small program that outputs a message  on  the  system
console to inform the operator to that effect.  If block 0 of a volume
is bad, it is permissible to map virtual block 1 of the index file  to
some  other block.  In this case, obviously, the volume cannot be used
as a system volume.

[Standardization efforts are currently underway for the format of  the
boot  block.   When  this work is completed, a copy of or reference to
that standard will be included here.]



5.1.2  Home Block


                                                    ____  _____Virtual block 2 of the index file is the  volume's  home  block.   The
purpose  of  the  home  block  is  to identify the volume as Files-11,
establish the specific identity of the volume, and serve as the ground
zero  entry point into the volume's file structure.  The home block is
recognized as a home block by  the  presence  of  checksums  in  known
places and by the presence of predictable values in certain locations.

The home block is located on the first good block of  the  home  block
search sequence.  The search sequence is of the form

               1 + n * delta, n = 0, 1, 2, 3, 4 ......

Files-11 On-Disk Structure                                     Page 33


The home block search delta is  computed  from  the  geometry  of  the
volume  such  that,  if  the  volume  is viewed as a three dimensional
space, the search sequence will travel  approximately  down  the  body
diagonal of the space.  Since volume failures tend to occur across one
dimension, this minimizes the chance of a  single  failure  destroying
both home blocks of the volume.  The search delta is computed from the
volume  geometry,  expressed  in  sectors,  tracks   (surfaces),   and
cylinders, according to the following rules, to handle the cases where
one or two dimensions of the volume have a size of 1.

          Geometry:     Delta

          s x 1 x 1:    1
          1 x t x 1:    1
          1 x 1 x c:    1

          s x t x 1:    s+1
          s x 1 x c:    s+1
          1 x t x c:    t+1

          s x t x c:    (t+1)*s+1

[Volumes are coming into  existence  whose  geometry  is  not  regular
(i.e.,  which  have  different numbers of sectors on different tracks)
due to density considerations.  The delta computation  algorithm  will
have to be amended to deal with such volumes in a reasonable way.]

In most cases, the home block is located on LBN 1.



5.1.3  Cluster Filler


If v, the cluster factor of the volume, is greater than  1,  then  the
next  v*2-2 blocks of the index file are copies of the home block used
to fill out the first two clusters of the index file.  Note that,  for
cluster factors greater than 1, this results in a wasted disk cluster.
The benefit of this technique is a much simpler rule for  finding  the
VBN of interesting parts of the index file.



5.1.4  Backup Home Block


The backup home block is a second  copy  of  the  home  block  located
farther down the home block search sequence.  It permits the volume to
be used even if the primary home block is destroyed.

In general, the backup home block should be allocated  on  the  second
good  block  of the search sequence.  If it is not, then all preceding
blocks on the sequence must not be available for allocation.  This  is
to   prevent   the  situation  of  a  malicious  user  constructing  a
counterfeit index file, which would be used if the primary home  block

Files-11 On-Disk Structure                                     Page 34


ever went bad.

The cluster which contains the backup home block is  mapped  into  the
index  file as virtual blocks v*2+1 through v*3, where v is the volume
cluster factor.  Observe that the backup home  block  may  be  located
anywhere  within  this  cluster,  because  there  is  no hard and fast
relationship between the cluster factor and  the  volume's  track  and
cylinder  boundaries.  The entire cluster is therefore filled out with
copies of the home block.



5.1.5  Backup Index File Header


The next cluster of the index file contains a backup copy of the index
file  header, so that data on the volume can be recovered if the index
file header goes bad.   The  cluster  occupies  virtual  blocks  v*3+1
through  v*4,  where  v  is the volume cluster factor.  The LBN of the
backup index file header is stored in location HM2$L_ALTIDXLBN in  the
home  block.  The backup index file header occupies the first block of
this cluster; the remaining blocks are not used and their contents are
undefined.



5.1.6  Index File Bitmap


    _____ ____ ______The index file bitmap is  used  to  control  the  allocation  of  file
numbers (and hence file headers).  It is simply a bit string of length
n, where n is the maximum number of  files  permitted  on  the  volume
(contained  in  offset  HM2$L_MAXFILES in the home block).  The bitmap
spans over as many blocks as is necessary to hold it, i.e., max number
of  files divided by 4096 and rounded up.  The number of blocks in the
bitmap is contained in offset HM2$W_IBMAPSIZE of the home block.

The bits in the index file bitmap are numbered sequentially from 0  to
n-1  in the obvious manner, i.e., from right to left in each byte, and
in order of increasing byte address.  Bit j is used to represent  file
number  j+1:  if the bit is 1, then that file number is in use; if the
bit is 0, then that file number is not in use and may be assigned to a
newly  created  file.   Note that the index file bitmap is not used to
determine whether a header is valid when accessing an  existing  file;
that is done solely with the contents of the header itself.

The index file bitmap starts at virtual block v*4+1 of the index  file
and  continues  through  VBN v*4+m, where m is the number of blocks in
the bitmap, and v is the storage map cluster factor.  It is located at
the  logical  block  indicated  by  offset  HM2$L_IBMAPLBN in the home
block.

Files-11 On-Disk Structure                                     Page 35


5.1.7  File Headers


The rest of the index file contains  all  the  file  headers  for  the
volume.   The  first  16  file  headers (for file numbers 1 to 16) are
logically contiguous with the index file bitmap  to  facilitate  their
location; the rest may be allocated wherever the file system sees fit.
Thus the first 16 file headers may be located from data  in  the  home
block  (HM2$W_IBMAPSIZE  and  HM2$L_IBMAPLBN)  while  the rest must be
located through the mapping data in the index file header.   The  file
header  for file number n is located at virtual block v*4+m+n (where m
is the number of blocks in the index file bitmap, and v is the storage
map cluster factor).

The end of file mark for the index file is located at  or  beyond  the
last  file header ever used.  All header blocks located before the EOF
are subject to validation when used to create  a  new  file.   If  the
block  contains  garbage,  the  new header is assigned a file sequence
number of 1, being the first use of this header block.  If  the  block
contains  a deleted file header, the new header is assigned a sequence
number one higher than the  one  contained  in  the  block.   A  block
containing  a  valid  file  header  must never be used to create a new
file, even if it is marked  free  in  the  index  file  bitmap.   This
prevents  files  from  being  lost  if bits are dropped in the bitmap.
Index file blocks beyond the EOF are assumed to  contain  garbage  for
the purpose of creating new file headers.

In all cases, the file header is the final authority on  the  volume's
file  structure.  If a volume has been damaged, reconstruction (of the
bitmaps, directories, etc.) may be done using the file headers as  the
source of file structure information.



5.1.8  Index File Layout


The following is a sketch of the blocks in the  index  file.   Observe
that  this  illustration  assumes a storage map cluster factor greater
than 2.


          |-------------------|---
          |                   |   \
          |       Boot        |    |  
          |       Block       |    |  
          |                   |    |  
          |-------------------|    |  
          |                   |    |  
          |       Home        |    |  
          |       Block       |    | Cluster 1
          |                   |    |
          |-------------------|    |
          |       More        |    |
          |       Home        |    |

Files-11 On-Disk Structure                                     Page 36


          |      Blocks       |    |
          |         :         |    |
          |         :         |    |
          |         :         |   /
          |-------------------|---
          |                   |   \ 
          |       More        |    |
          |       Home        |    |
          |      Blocks       |    | Cluster 2
          |         :         |    |
          |         :         |    |
          |         :         |   /
          |-------------------|---
          |      Backup       |   \ 
          |       Home        |    |
          |       Block       |    |
          |                   |    |
          |-------------------|    |
          |       More        |    | Cluster 3
          |       Home        |    |
          |      Blocks       |    |
          |         :         |    |
          |         :         |    |
          |         :         |   / 
          |-------------------|---
          |      Backup       |   \ 
          |       Index       |    |
          |       File        |    |
          |      Header       |    |
          |-------------------|    |
          |                   |    | Cluster 4
          |                   |    |
          |       (not)       |    |
          |      (used)       |    |
          |                   |    |
          |                   |   /
          |-------------------|---
          |                   |   \
          |       Index       |    |
          |       File        |    |
          |      Bitmap       |    |
          |                   |    |
          |                   |    |
          |-------------------|    | Contiguous
          |                   |    |
          |        16         |    |
          |       File        |    |
          |      Headers      |    |
          |                   |    |
          |                   |   /
          |-------------------|---
          |                   |
          |                   |
          |                   |
          |       Lots        |

Files-11 On-Disk Structure                                     Page 37


          |       More        |
          |       File        |
          |      Headers      |
          |                   |
          |                   |
          |                   |
          |                   |
          |-------------------|



5.1.9  Home Block Details

The following is a detailed description of the home block.  Note  that
all  copies of the volume's home block contain the same data, with the
exception of the cells containing the block's VBN and LBN.



5.1.9.1  HM2$L_HOMELBN - 4 Bytes        Home Block LBN


          This longword contains the  logical  block  number  of  this
          particular copy of the home block.



5.1.9.2  HM2$L_ALHOMELBN - 4 Bytes      Alternate Home Block LBN


          This longword contains the LBN  of  the  volume's  secondary
          home block.  One may determine, when scanning the home block
          sequence, whether the block read is the primary or secondary
          home  block  by comparing HM2$L_HOMELBN and HM2$L_ALHOMELBN.
          This value must be non-zero for a valid home block.



5.1.9.3  HM2$L_ALTIDXLBN - 4 Bytes      Backup Index File Header LBN


          This longword contains the logical block on which the backup
          index  file  header is located.  This value must be non-zero
          for a valid home block.



5.1.9.4  HM2$W_STRUCLEV - 2 Bytes       Structure Level and Version


          The volume structure level and version is used  to  identify
          different  versions of Files-11 as they affect the structure
          of all parts of the volume except  the  file  header.   This
          permits upwards compatibility of file structures as Files-11
          evolves, in that the structure  level  word  identifies  the

Files-11 On-Disk Structure                                     Page 38


          version  of  Files-11  that  created this particular volume.
          This document describes structure level 2 of Files-11.   The
          high  byte  of HM2$W_STRUCLEV must contain the value 2.  The
          low byte contains the version number, which must be  greater
          or  equal  to  1.   The  version  number will be incremented
          whenever compatible  additions  are  made  to  the  Files-11
          structure  that  may  be safely ignored by an old version of
          the file system.   This  document  describes  version  1  of
          structure level 2.



5.1.9.5  HM2$W_CLUSTER - 2 Bytes        Storage Bitmap Cluster Factor


          This word contains the cluster factor used  in  the  storage
          bitmap  file.   The  cluster  factor is the number of blocks
          represented by each bit in the storage bitmap.   This  value
          is also referred to as the volume cluster factor.



5.1.9.6  HM2$W_HOMEVBN - 2 Bytes        Home Block VBN


          This word contains the virtual block  that  this  particular
          copy  of  the  home  block occupies in the index file.  This
          value must be non-zero for a valid home block.



5.1.9.7  HM2$W_ALHOMEVBN - 2 Bytes      Backup Home Block VBN


          This word contains the virtual block number that the cluster
          containing  the  secondary  home block occupies in the index
          file.  The contents of this word is v*2+1, where  v  is  the
          storage map cluster factor.



5.1.9.8  HM2$W_ALTIDXVBN - 2 Bytes      Backup Index File Header VBN


          This word contains the virtual block number that the  backup
          index  file header occupies in the index file.  The contents
          of this word is v*3+1, where v is the  storage  map  cluster
          factor.



5.1.9.9  HM2$W_IBMAPVBN - 2 Bytes       Index File Bitmap VBN


          This word contains the starting virtual block number of  the

Files-11 On-Disk Structure                                     Page 39


          index  file  bitmap.  The contents of this word is the value
          v*4+1, where v is the storage map cluster factor.



5.1.9.10  HM2$L_IBMAPLBN - 4 Bytes      Index File Bitmap LBN


          This longword contains the starting logical block address of
          the  index file bitmap.  Once the home block of a volume has
          been found, it is this value that  provides  access  to  the
          rest  of  the index file and to the volume.  This value must
          be non-zero for a valid home block.



5.1.9.11  HM2$L_MAXFILES - 4 Bytes      Maximum Number of Files


          This longword contains the maximum number of files that  may
          be  present  on  the volume at any time.  This value must be
          greater than the contents of  HM2$W_RESFILES  for  the  home
          block  to  be valid.  If the maximum number of files is less
          than 65536, then the third word  of  File  ID's  referencing
          files  on  this volume is simply the relative volume number,
          and the volume set of which this  volume  is  a  member  may
          contain up to 65535 volumes.  If the maximum number of files
          is greater than or equal to 65536, however,  then  the  high
          byte  of the third word of File ID's is the high byte of the
          file number, and the volume set may consist  of  up  to  255
          volumes.   Under  no circumstances may the maximum number of
          files be greater than 2**24-1.



5.1.9.12  HM2$W_IBMAPSIZE - 2 Bytes     Index File Bitmap Size


          This 16 bit word contains the number of blocks that make  up
          the  index  file  bitmap.  This value must be non-zero for a
          valid home block.



5.1.9.13  HM2$W_RESFILES - 2 Bytes      Number of Reserved Files


          This word contains the number of of  reserved  file  on  the
          volume.   The  file sequence number of each reserved file is
          always equal to its file number.  Reserved files may not  be
          deleted.   This word must contain a minimum value of 5 to be
          valid.

Files-11 On-Disk Structure                                     Page 40


5.1.9.14  HM2$W_DEVTYPE - 2 Bytes       Disk Device Type


          This word is an index identifying  the  type  of  disk  that
          contains  this  volume.  It is currently not used and always
          contains 0.



5.1.9.15  HM2$W_RVN - 2 Bytes Relative Volume Number


          This word contains the  relative  volume  number  that  this
          volume  has been assigned in a volume set.  If the volume is
          not part of a volume set, then this word contains zero.



5.1.9.16  HM2$W_SETCOUNT - 2 Bytes      Number of Volumes


          This word contains the total number of volumes in a  tightly
          coupled  volume set if the contents of HM2$W_RVN is 1 (i.e.,
          if this volume is the  first  volume  of  the  volume  set).
          Otherwise, this word contains zero.



5.1.9.17  HM2$W_VOLCHAR - 2 Bytes       Volume Characteristics


          This word contains bits  which  provide  additional  control
          over access to the volume.  The following bits are defined:

          HM2$V_READCHECK  Set if the volume is to  be  read  checked.
                           All  block  reads done on this volume, both
                           for data and for file  structure,  will  be
                           performed   with   a   read,   read-compare
                           sequence to insure data integrity.

          HM2$V_WRITCHECK  Set if the volume is to be  write  checked.
                           All  block writes done on this volume, both
                           for data and for file  structure,  will  be
                           performed   with   a   write,  read-compare
                           sequence to insure data integrity.

          HM2$V_ERASE      Set if all files on the volume  are  to  be
                           erased when they are deleted.

          HM2$V_NOHIGHWATER Set if highwater mark enforcement is to be
                           disabled on the volume.

Files-11 On-Disk Structure                                     Page 41


5.1.9.18  HM2$L_VOLOWNER - 4 Bytes      Volume Owner UIC


          This longword contains the binary UIC of the  owner  of  the
          volume.   The  format  is the same as that of the file owner
          UIC stored in the file header.



5.1.9.19  4 Bytes (not used)

5.1.9.20  HM2$W_PROTECT - 2 Bytes       Volume Protection Code


          This word  contains  the  protection  code  for  the  entire
          volume.  All operations on all files on the volume must pass
          both  the  volume  and  the  file  protection  check  to  be
          permitted.   Accessors  to  the  volume are categorized into
          system, owner, group, and world with respect to  the  volume
          owner  UIC  in the same manner as for file protection.  Each
          category is controlled by the familiar four bit field.   The
          four access modes are bit encoded as follows:

          Bit 0     Set to deny reading files
          Bit 1     Set to deny writing existing files
          Bit 2     Set to deny creating files
          Bit 3     Set to deny deleting files



5.1.9.21  HM2$W_FILEPROT - 2 Bytes      Default File Protection


          This word contains the file protection that will be assigned
          to  files  created  on  this volume if no file protection is
          specified by the user or the operating system.



5.1.9.22  2 Bytes (not used)

5.1.9.23  HM2$W_CHECKSUM1 - 2 Bytes     First Checksum


          This word is an additive checksum of all  entries  preceding
          in  the  home  block  (i.e., all those listed above).  It is
          computed by the same sort of algorithm as  the  file  header
          checksum (see section 3.5.7.1).



5.1.9.24  HM2$Q_CREDATE - 8 Bytes       Volume Creation Date


          This area contains the date and time  that  the  volume  was

Files-11 On-Disk Structure                                     Page 42


          initialized.   It  is  in the same binary format used in the
          file header (see section 3.5.3.3).



5.1.9.25  HM2$B_WINDOW - 1 Byte         Default Window Size


          This byte contains the number  of  retrieval  pointers  that
          will  be  used  for  the "window" (in core file access data)
          when files are accessed on  the  volume,  if  not  otherwise
          specified by the accessor.



5.1.9.26  HM2$B_LRU_LIM - 1 Byte        Directory Pre-access Limit


          This byte contains a count of the number of  directories  to
          be stored in the file system's directory access cache.  More
          generally, it is an estimate of  the  number  of  concurrent
          users  of  the  volume and its use may be generalized in the
          future.



5.1.9.27  HM2$W_EXTEND - 2 Bytes        Default File Extend


          This word  contains  the  number  of  blocks  that  will  be
          allocated  to  a  file when a user extends the file and asks
          for the system default value for allocation.



5.1.9.28  HM2$Q_RETAINMIN - 8 Bytes     Minimum File Retention Period

          This field contains the minimum length of time that  a  file
          will be retained by a file expiration system after that file
          is last accessed.  Its value is expressed  in  the  standard
          delta  time  format;  i.e.,  minus  the  time  in  tenths of
          microseconds.



5.1.9.29  HM2$Q_RETAINMAX - 8 Bytes     Maximum File Retention Period

          This field contains the maximum length of time that  a  file
          will be retained by a file expiration system after that file
          is last accessed.  Its value is likewise  expressed  in  the
          standard delta time format.

          The minimum and maximum retention fields are  used  together
          as  follows:   When  a  file  is accessed, if the sum of the
          current time plus the minimum retention period  exceeds  the

Files-11 On-Disk Structure                                     Page 43


          current  expiration  date  of  the  file,  then  the  file's
          expiration date is reset to the sum of the current time plus
          the  maximum  retention  period.   The  net  effect  of this
          process is that the frequency of update  of  the  expiration
          date  of  a  frequently  accessed  file is determined by the
          difference  between  the  minimum  and   maximum   retention
          periods.



5.1.9.30  HM2$Q_REVDATE - 8 Bytes       Volume Revision Date

          This field contains the date and  time  at  which  the  last
          significant  modification  was  made  to  the  volume.  Such
          modifications include  copying  via  a  full  backup,  state
          change of a volume shadow set, etc.



5.1.9.31  HM2$R_MIN_CLASS - 20 Bytes    Minimum Security Class

          This field contains a classification  mask  that  represents
          the  minimum  security and integrity classification of files
          that may be created on this volume.  The structure  of  this
          field  is  the  same  as its counterpart in the file header,
          described in section 3.5.2.22.



5.1.9.32  HM2$R_MAX_CLASS - 20 Bytes    Maximum Security Class

          This field contains a classification  mask  that  represents
          the  maximum  security and integrity classification of files
          that may be created on this volume.  The structure  of  this
          field  is  the  same  as its counterpart in the file header,
          described in section 3.5.2.22.



5.1.9.33  320 Bytes                     Not Used

5.1.9.34  HM2$L_SERIALNUM - 4 Bytes     Media Serial Number

          This field contains the binary serial number of the physical
          medium on which the volume is located.



5.1.9.35  HM2$T_STRUCNAME - 12 Bytes    Structure Name


          This area contains the ASCII name of the volume set to which
          this volume belongs, padded out to 12 bytes with spaces.  If
          this volume is not a member of a volume set, then this  area
          is filled with spaces.

Files-11 On-Disk Structure                                     Page 44


5.1.9.36  HM2$T_VOLNAME - 12 Bytes      Volume Name


          This area contains the volume label in ASCII.  It is  padded
          out to 12 bytes with spaces.



5.1.9.37  HM2$T_OWNERNAME - 12 Bytes    Volume Owner


          This area contains an ASCII string identifying the owner  of
          the  volume.   The  area  is  padded  out  to  12 bytes with
          trailing spaces.



5.1.9.38  HM2$T_FORMAT - 12 Bytes       Format Type


          This field contains the ASCII string "DECFILE11B" padded out
          to  12 bytes with spaces.  It identifies the volume as being
          of Files-11 format, structure level 2.



5.1.9.39  2 Bytes                       Not Used

5.1.9.40  HM2$W_CHECKSUM2 - 2 Bytes     Second Checksum


          This word is the last word of the home block.   It  contains
          an  additive checksum of the preceding 255 words of the home
          block, computed according to the algorithm listed in section
          3.5.7.1.

Files-11 On-Disk Structure                                     Page 45


5.1.9.41  Home Block Layout

                |---------------------------------------|
                |                                       |   HM2$L_HOMELBN
                |--         LBN of This Block         --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$L_ALHOMELBN
                |--    LBN of Secondary Home Block    --|
                |                                       |    
                |---------------------------------------|
                |            LBN of Secondary           |   HM2$L_ALTIDXLBN
                |--                                   --|
                |           Index File Header           |    
                |---------------------------------------|
                |        Volume Structure Level         |   HM2$W_STRUCLEV
                |---------------------------------------|
                |     Storage Bitmap Cluster Factor     |   HM2$W_CLUSTER
                |---------------------------------------|
                |           VBN of This Block           |   HM2$W_HOMEVBN
                |---------------------------------------|
                |         Backup Home Block VBN         |   HM2$W_ALHOMEVBN
                |---------------------------------------|
                |        Backup Index Header VBN        |   HM2$W_ALTIDXVBN
                |---------------------------------------|
                |         Index File Bitmap VBN         |   HM2$W_IBMAPVBN
                |---------------------------------------|
                |              Index File               |   HM2$L_IBMAPLBN
                |--                                   --|
                |              Bitmap LBN               |    
                |---------------------------------------|
                |                                       |   HM2$L_MAXFILES
                |--      Maximum Number of Files      --|
                |                                       |   
                |---------------------------------------|
                |        Index File Bitmap Size         |   HM2$W_IBMAPSIZE
                |---------------------------------------|
                |       Number of Reserved Files        |   HM2$W_RESFILES
                |---------------------------------------|
                |           Disk Device Type            |   HM2$W_DEVTYPE
                |---------------------------------------|
                |         Relative Volume Number        |   HM2$W_RVN
                |---------------------------------------|
                |       Number of Volumes in Set        |   HM2$W_SETCOUNT
                |---------------------------------------|
                |        Volume Characteristics         |   HM2$W_VOLCHAR
                |---------------------------------------|
                |                                       |   HM2$L_VOLOWNER
                |--         Volume Owner UIC          --|
                |                                       |   
                |---------------------------------------|
                |                                       |
                |--            (not used)             --|
                |                                       |   
                |---------------------------------------|

Files-11 On-Disk Structure                                     Page 46


                |           Volume Protection           |   HM2$W_PROTECT
                |---------------------------------------|
                |        Default File Protection        |   HM2$W_FILEPROT
                |---------------------------------------|
                |              (not used)               |
                |---------------------------------------|
                |            First Checksum             |   HM2$W_CHECKSUM1
                |---------------------------------------|
                |                                       |   HM2$Q_CREDATE
                |--                                   --|
                |                                       |   
                |--       Volume Creation Date        --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |-------------------|-------------------|
HM2$B_LRU_LIM   |  Directory Limit  | Def. Window Size  |   HM2$B_WINDOW
                |-------------------|-------------------|
                |          Default File Extend          |   HM2$W_EXTEND
                |---------------------------------------|
                |                                       |   HM2$Q_RETAINMIN
                |--                                   --|
                |              Minimum File             |   
                |--          Retention Period         --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$Q_RETAINMAX
                |--                                   --|
                |              Maximum File             |   
                |--          Retention Period         --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$Q_REVDATE
                |--                                   --|
                |                                       |   
                |--       Volume Revision Date        --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$R_MIN_CLASS
                |--                                   --|
                |                                       |   
                |--       Minimum File Security       --|
                |          Classification Level         |   
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$R_MAX_CLASS

Files-11 On-Disk Structure                                     Page 47


                |--                                   --|
                |                                       |   
                |--       Maximum File Security       --|
                |          Classification Level         |   
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |                                       |    
                |                                       |    
                |                                       |    
                |                                       |    
                |              (not used)               |
                |                                       |    
                |                                       |    
                |                                       |    
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$L_SERIALNUM
                |--        Media Serial Number        --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$T_STRUCNAME
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |--         Volume Set Name           --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$T_VOLNAME
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |--            Volume Name            --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$T_OWNERNAME
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |--           Volume Owner            --|
                |                                       |    
                |--                                   --|

Files-11 On-Disk Structure                                     Page 48


                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$T_FORMAT
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |--            Format Type            --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |              (not used)               |
                |---------------------------------------|
                |            Second Checksum            |   HM2$W_CHECKSUM2
                |---------------------------------------|



5.2  Storage Bitmap File

The storage bitmap file is File ID 2,2.  It is listed in  the  MFD  as
BITMAP.SYS;1.   The  storage  bitmap  is used to control the available
                                        _______  _______  _____space on a volume.  It consists  of  a  storage  control  block  which
contains  summary  information about the volume, and the bitmap itself
which lists the availablilty of individual blocks.  This file has  the
record  format  of  512  byte  fixed  length records, with no carriage
control.  The end of file mark is positioned  to  point  to  the  last
block used.  The storage bitmap file must be contiguous.



5.2.1  Storage Control Block


Virtual block 1 of the storage bitmap is the  storage  control  block.
It   contains   summary  information  about  the  volume.   Note  that
implementation of some of the features in the  storage  control  block
may require it to be written at mount and dismount.



5.2.1.1  SCB$W_STRUCLEV - 2 Bytes       Storage Map Structure Level


          This word  contains  the  structure  level  of  the  storage
          control  block.   The  high  byte  contains  the  value 2 to
          indicate Files-11 structure level 2.  The low byte  contains
          the  version  number, which must be equal to or greater then
          1.

Files-11 On-Disk Structure                                     Page 49


5.2.1.2  SCB$W_CLUSTER - 2 Bytes        Storage Map Cluster Factor


          This word contains the storage map  cluster  factor  of  the
          volume.   Its  contents  are  identical  to  the contents of
          HM2$W_CLUSTER in the home block.   It  is  placed  here  for
          convenience.



5.2.1.3  SCB$L_VOLSIZE - 4 Bytes        Volume Size


          This field contains the volume  size  expressed  in  logical
          blocks.



5.2.1.4  SCB$L_BLKSIZE - 4 Bytes        Blocking Factor


          This field contains the blocking factor of the volume; i.e.,
          the  number  of  physical blocks or sectors that make up one
          logical block.



5.2.1.5  SCB$L_SECTORS - 4 Bytes        Sectors Per Track


          This field contains the number of  logical  blocks  in  each
          track of the volume.



5.2.1.6  SCB$L_TRACKS - 4 Bytes         Tracks Per Cylinder


          This field contains the number of tracks contained  in  each
          cylinder of the volume.



5.2.1.7  SCB$L_CYLINDER - 4 Bytes       Number of Cylinders


          This field contains the total number  of  cylinders  on  the
          volume.   The  above  three quantities are present to assist
          optimized allocation of space on physical boundaries in  the
          volume.

Files-11 On-Disk Structure                                     Page 50


5.2.1.8  SCB$L_STATUS - 4 Bytes         Status Word


          This word contains the following status bits:




5.2.1.9  SCB$L_STATUS2 - 4 bytes        Secondary Status

          This word contains a copy of the  primary  status  word  for
          deferred use.



5.2.1.10  SCB$W_WRITECNT - 2 Bytes      Writer Count

          This word contains the number of  independent  systems  that
          currently have the volume mounted for write.



5.2.1.11  SCB$T_VOLOCKNAME - 12 Bytes   Volume Lock Name

          This field contains a unique name which is used  as  a  root
          for synchronization resource names for the volume.



5.2.1.12  SCB$Q_MOUNTTIME - 4 Bytes     Time of Last Mount

          This field contains the date and time of the last  time  the
          volume  was  mounted  for  write.   It  is  expressed in the
          standard time format.



5.2.1.13  456 Bytes                     (not used)

5.2.1.14  SCB$W_CHECKSUM - 2 Bytes      Block Checksum


          This word contains the ubiquitous  block  checksum.   It  is
          computed  using  the  same  algorithm  as  the  file  header
          checksum (section 3.5.7.1).



5.2.1.15  Storage Control Block Layout



                |---------------------------------------|
                |            Structure Level            |   SCB$W_STRUCLEV
                |---------------------------------------|

Files-11 On-Disk Structure                                     Page 51


                |      Storage Map Cluster Factor       |   SCB$W_CLUSTER
                |---------------------------------------|
                |                                       |   SCB$L_VOLSIZE
                |--       Volume Size in Blocks       --|
                |                                       |   
                |---------------------------------------|
                |                                       |   SCB$L_BLKSIZE
                |--          Blocking Factor          --|
                |                                       |   
                |---------------------------------------|
                |                                       |   SCB$L_SECTORS
                |--         Sectors Per Track         --|
                |                                       |   
                |---------------------------------------|
                |                                       |   SCB$L_TRACKS
                |--        Tracks Per Cylinder        --|
                |                                       |   
                |---------------------------------------|
                |                                       |   SCB$L_CYLINDER
                |--        Cylinders on Volume        --|
                |                                       |   
                |---------------------------------------|
                |                                       |   SCB$L_STATUS
                |--           Volume Status           --|
                |                                       |   
                |---------------------------------------|
                |                                       |   SCB$L_STATUS2
                |--      Secondary Volume Status      --|
                |                                       |   
                |---------------------------------------|
                |          Volume Writer Count          |   SCB$W_WRITECNT
                |---------------------------------------|
                |                                       |   SCB$T_VOLOCKNAME
                |--                                   --|   
                |                                       |   
                |--                                   --|   
                |         Volume Synchronization        |   
                |--             Lock Name             --|   
                |                                       |   
                |--                                   --|   
                |                                       |   
                |--                                   --|   
                |                                       |   
                |---------------------------------------|
                |                                       |   SCB$Q_MOUNTTIME
                |--                                   --|   
                |             Time of Last              |   
                |--           Initial Mount           --|   
                |                                       |   
                |--                                   --|   
                |                                       |   
                |---------------------------------------|
                |                                       |   
                |                                       |   
                |                                       |   

Files-11 On-Disk Structure                                     Page 52


                |                                       |   
                |                                       |   
                |              (not used)               |   
                |                                       |   
                |                                       |   
                |                                       |   
                |                                       |   
                |                                       |   
                |---------------------------------------|
                |            Block Checksum             |   SCB$W_CHECKSUM
                |---------------------------------------|



5.2.2  Storage Bitmap

Virtual blocks 2 through n+1 are the storage  bitmap  itself.   It  is
best viewed as a bit string of length m, numbered from 0 to m-1, where
m is the total number of allocatable clusters on the volume rounded up
to the next multiple of 4096.  Each cluster contains v logical blocks,
where v is the storage map cluster factor (also  referred  to  as  the
volume cluster factor) contained in location HM2$W_CLUSTER in the home
block.  The bits are addressed in the usual manner  (packed  right  to
left  in sequentially numbered bytes).  Since each virtual block holds
4096 bits, n blocks, where n = m/4096, are used to  hold  the  bitmap.
Bit  j  of the bitmap represents logical blocks j*v through j*v+v-1 of
the volume; if the bit is set, the blocks  are  free;  if  clear,  the
blocks  are  allocated.   Clearly  the  last  k bits of the bitmap are
always clear, where k is the difference between the true size  of  the
volume and m, the length of the bitmap.

Rounding the storage map file up to the next multiple  of  the  volume
cluster  factor  may  result  in  some unused blocks at the end of the
file.  The end of file mark points to the last block used.



5.3  Bad Block File

The bad block file is File ID  3,3.   It  is  listed  in  the  MFD  as
BADBLK.SYS;1.   The  bad block file is simply a file containing all of
the known bad blocks on the volume.  This file has the  record  format
of 512 byte fixed length records, with no carriage control.

On  disks  containing  a  bad  block  descriptor  (see  following  two
sections),  the  last  track  of  the  volume  should occupy the first
several clusters of the bad block file.  This  ensures  that  the  bad
block  data  is available to software in a file structured manner, and
is preserved for future re-initialization of the volume.

The end of file mark may be placed as the operating system's bad block
handling  strategy  finds  useful.  Volume initialization should place
the EOF at the end of the bad blocks found during initialization.   At
all times, the EOF should at least point past the bad block descriptor
data.

Files-11 On-Disk Structure                                     Page 53


5.3.1  Factory Bad Block Descriptor

Many DEC supplied disks preceding DSA disks have  a  factory  supplied
format  that  lists  the  known bad blocks in the volume's last track.
Disks of this type include the RK06,  RK07,  RL02,  RP06,  RM03,  etc.
This  track  contains  redundantly  recorded  descriptions  of the bad
blocks on the volume, as described in DEC STD.   144,  "Disk  Standard
for Recording and Handling Manufacturing Detected Bad Sectors".



5.3.2  Software Bad Block Descriptor

For disks that do not have  factory  last  track  bad  block  data,  a
software  generated  bad  block  map  may  be  supplied.  It is always
located on the last good block of the volume.  The software bad  block
descriptor  is  most  of a Files-11 Structure Level 1 header map area.
The first two bytes contain the constants 1 and 3, respectively.   The
third byte contains the number of words that contain data.  The fourth
byte contains the number of words available for bad block  data.   The
last  word  of  the  block  contains the usual additive checksum.  The
retrieval pointers  are  structure  level  1  format  1  pointers,  as
described below.


Bad Block Descriptor Layout


                |-------------------|-------------------|
BBM$B_LBNSIZE   |         3         |         1         |   BBM$B_COUNTSIZE
                |-------------------|-------------------|
BBM$B_AVAIL     | Map Words Avail.  | Map Words in Use  |   BBM$B_INUSE
                |-------------------|-------------------|
                |                                       |   BBM$C_POINTERS
                |                                       |
                |                                       |
                |          Retrieval Pointers           |    
                |                                       |
                |                                       |
                |                                       |
                |---------------------------------------|
                |            Block Checksum             |   BBM$W_CHECKSUM
                |---------------------------------------|


Each retrieval pointer is four bytes in length.  Byte 1  contains  the
high  order  bits  of the 24 bit LBN.  Byte 2 contains the count field
(in excess 1 format), and bytes 3 and 4 contain the low 16 bits of the
LBN.

                |-------------------|-------------------|
BBM$B_COUNT     |    Block Count    |  High Order LBN   |   BBM$B_HIGHLBN
                |-------------------|-------------------|
                |             Low Order LBN             |   BBM$W_LOWLBN
                |---------------------------------------|

Files-11 On-Disk Structure                                     Page 54


5.4  Master File Directory

The master file directory is File ID 4,4.  It is  listed  in  the  MFD
(itself)  as  000000.DIR;1.   The  MFD  is  the  root  of the volume's
directory structure.  It lists the reserved files, plus  whatever  the
user  chooses  to  enter.   The  format  of the MFD is the same as all
directory files,  and  is  described  in  section  4.3.   In  the  UFD
structures  described  in  sections  4.1.1 and 4.1.2, the MFD contains
entries for all top level user file directories.



5.5  Core Image File

The core image file is File ID 5,5.   It  is  listed  in  the  MFD  as
CORIMG.SYS;1.   Its use is operating system dependent.  In general, it
provides a file of known File ID for the use of the operating  system,
for  use  as  a  swap area, for example, or as a monitor overlay area,
etc.  This file has  the  record  format  of  512  byte  fixed  length
records, with no carriage control.  The end of file mark is positioned
to point to the physical end of file.



5.6  Volume Set List

The volume set list is File ID 6,6.   It  is  listed  in  the  MFD  as
VOLSET.SYS;1.   It  is  used  only on relative volume one of a tightly
coupled volume set.  There, it contains a list of the volume labels of
the  volumes contained in this volume set.  The format of this file is
64 byte fixed length records with implied carriage control.  The first
12  bytes  of  record  1 contain the structure name of the volume set.
The first 12 bytes of record n contain the volume  label  of  relative
volume  n-1.   The  remaining 52 bytes of each record are reserved for
future use.



5.7  Continuation File

The standard continuation file is File ID 7,7.  It is  listed  in  the
MFD  as CONTIN.SYS;1.  It is used as the extension File ID when a file
crosses from one volume of a loosely coupled volume  set  to  another.
The  purpose  of this reserved File ID is allow a multi-volume file to
be written sequentially with  only  one  volume  mounted  at  a  time.
Ordinarily,  when  a  file  is  extended  onto another volume, the new
header must be created first to obtain the  new  File  ID  before  the
extension  linkage  in  the current header can be written.  The use of
this reserved File ID allows the extension linkage to be written  with
a known constant before the next volume is even on line.

Files-11 On-Disk Structure                                     Page 55


5.8  Backup Log File

The backup log file is File ID 8,8,0.  It is  listed  in  the  MFD  as
BACKUP.SYS;1.   This file contains a history of volume and incremental
backups performed on the volume.  The format of this file is  64  byte
fixed  length  records.   No  implementations  of  Files-11  currently
support the backup log file, and its contents is at present undefined.



5.9  Pending Bad Block Log File

The pending bad block log file is File ID 9,9,0.  It is listed in  the
MFD  as BADLOG.SYS;1.  This file contains a list identifying suspected
bad blocks on the volume that  are  not  currently  contained  in  the
volume's  bad  block  file.   The format of this file is 16 byte fixed
length records.  Each record represents one bad  block,  and  has  the
following format:


                |---------------------------------------|
                |                                       |   PBB$W_FID
                |--              File ID              --|
                |               containing              |
                |--             bad block             --|
                |                                       |
                |-------------------|-------------------|
PBB$B_COUNT     |    Error Count    |      Flags        |   PBB$B_FLAGS
                |-------------------|-------------------|
                |                                       |   PBB$L_VBN
                |--          VBN within file          --|
                |                                       |
                |---------------------------------------|
                |                                       |   PBB$L_LBN
                |--                LBN                --|
                |                                       |
                |---------------------------------------|


The following bits are defined in the flags byte:

          PBB$V_READERR    Set if a read error has  occurred  on  this
                           block.

          PBB$V_WRITERR    Set if a write error has occurred  on  this
                           block.



6  Sequential Record File Structure

The Files-11 structure supports  several  sequential  record  formats,
which  are  described  in  this  section.   These  record  formats are
implemented by  the  record  support  packages  of  various  operating
systems,  such  as  FCS-11,  RMS-11,  and  VAX-11 RMS.  Record control

Files-11 On-Disk Structure                                     Page 56


information is maintained in the file's record  attributes  area,  and
embedded within the data blocks.

Other record formats (such as ISAM, direct, DBMS, etc.) are  supported
by  various operating systems.  Their structure is not covered by this
specification.



6.1  File Attributes

The record control information that applies to the file as a whole  is
kept in the file's record attributes area (FH2$W_RECATTR).  This block
contains the following fields:



6.1.1  FAT$B_RTYPE - 1 Byte             Record Type


          This byte identifies the file organization and record format
          of the file.  It is devided into two four bit subfields:

       FAT$V_RTYPE - 4 Bits             Record Format

          This field identifies the format of the records in the file.
          It may contain one of the following values:

          FAT$C_UNDEFINED  Undefined record format.  Record structure,
                           if  any,  is  supplied  by  the application
                           processing  the  file  by  specifying   the
                           number  of bytes to be read or written with
                           each record operation.

          FAT$C_FIXED      Fixed length records.  All records are  the
                           same  length, and stored with no additional
                           intervening record control information.

          FAT$C_VARIABLE   Variable  length  records.    Records   are
                           variable  in  length  from 1 to 32767 bytes
                           and are stored with a  16  bit  byte  count
                           preceding each record.

          FAT$C_VFC        Sequenced variable length records.  Records
                           are variable in length, and are stored with
                           a 16 bit byte  count,  plus  a  fixed  size
                           control  area,  preceding each record.  The
                           control  area  is  treated  as  an   entity
                           separate from the record.

          FAT$C_STREAM     General stream format.  Records are assumed
                           to  consist  of  ASCII  characters, and are
                           packed into the file's virtual blocks  with
                           no  additional  record control information.
                           The common line delimiter characters  (line

Files-11 On-Disk Structure                                     Page 57


                           feed,  form  feed,  vertical  tab, carriage
                           return, and escape) are treated  as  record
                           separators.

          FAT$C_STREAMLF   Line  feed  stream  format.   Records   are
                           assumed to consist of ASCII characters, and
                           are packed into the file's  virtual  blocks
                           with    no    additional   record   control
                           information.   Line  feed  characters   are
                           treated as record separators.

          FAT$C_STREAMCR   Carriage return stream format.  Records are
                           assumed to consist of ASCII characters, and
                           are packed into the file's  virtual  blocks
                           with    no    additional   record   control
                           information.   Carriage  return  characters
                           are treated as record separators.


       FAT$V_FILEORG - 4 Bits File Organization

          This field specifies the overall organization of  the  file.
          It contains one of the following values:

          FAT$C_SEQUENTIAL Sequential  file.   This  is   the   format
                           covered    in    this    section   of   the
                           specification.

          FAT$C_RELATIVE   Relative file.   This  file  format  allows
                           access  by  relative  record  number (e.g.,
                           Fortran direct access  and  Cobol  relative
                           file).

          FAT$C_INDEXED    Indexed  file.   This  file  format  allows
                           access  by  one  of  several indices (e.g.,
                           Cobol indexed access).

          FAT$C_DIRECT     Direct (hashed)  file.   This  file  format
                           allows  direct access to records by hashing
                           of a record key.   [Direct  files  are  not
                           currently  supported by any implementations
                           of Files-11.]



6.1.2  FAT$B_RATTRIB - 1 Byte           Record Attributes


          This byte contains record attribute bits  that  control  the
          handling  of  records under various contexts.  The following
          flag bits are defined:

          FAT$V_FORTRANCC  Use Fortran carriage control if  set.   The
                           first   byte   of  each  record  is  to  be
                           interpreted as a standard Fortran  carriage

Files-11 On-Disk Structure                                     Page 58


                           control character when the record is copied
                           to a carriage control device.

          FAT$V_IMPLIEDCC  Use implied carriage control if set.   When
                           the  file  is  copied to a carriage control
                           device, each record is to be preceded by  a
                           line   feed  and  followed  by  a  carriage
                           return.  Note that the FAT$V_FORTRANCC  and
                           FAT$V_IMPLIEDCC     bits    are    mutually
                           exclusive.

          FAT$V_PRINTCC    Use print  file  carriage  control.   Legal
                           only  if  the  record type is FAT$C_VFC and
                           the    size    of    the    control    area
                           (FAT$B_VFCSIZE)  is  two.   The leading two
                           byte  field  of  each  record  is  used  as
                           carriage  control  instead of as a sequence
                           number.  The first  and  second  bytes  are
                           used   as  leading  and  trailing  carriage
                           formatting,       respectively.         The
                           interpretation   of  the  carriage  control
                           bytes is described below in section 6.3.3.

                           If none of the  above  attributes  is  set,
                           then  the file has no carriage control, and
                           no additional formatting data is  added  to
                           the record contents when the file is copied
                           to a carriage control device.

          FAT$V_NOSPAN     Records do not cross  block  boundaries  if
                           set.   Generally,  there will be dead space
                           at the end  of  each  block;  how  this  is
                           handled  is explained in the description of
                           record formats in section 6.3.



6.1.3  FAT$W_RSIZE - 2 Bytes            Record Size


          In a fixed length record file, this word contains  the  size
          of  the records in bytes.  In a variable length record file,
          this word contains the size in bytes of the  longest  record
          in the file.



6.1.4  FAT$L_HIBLK - 4 Bytes            Highest VBN Allocated


          This 32 bit number is a  count  of  the  number  of  virtual
          blocks  allocated to the file.  For historical reasons, this
          quantity is stored in swapped  format;  that  is,  the  high
          order  16  bits occupy the first two bytes and the low order
          16 bits the second two bytes.

Files-11 On-Disk Structure                                     Page 59


6.1.5  FAT$L_EFBLK - 4 Bytes            End of File Block


          This 32 bit number is the VBN  at  which  the  end  of  file
          position  is  located.   This  value  is  likewise stored in
          swapped format.



6.1.6  FAT$W_FFBYTE - 2 Bytes           First Free Byte


          This word is a count of the number of bytes in  use  in  the
          virtual  block  containing  the end of file; i.e., it is the
          offset  to  the  first  byte  of  the  file  available   for
          appending.   Note  that an end of file that falls on a block
          boundary may be represented in either of two ways.   If  the
          file  contains precisely n blocks, FAT$L_EFBLK may contain n
                                                  __          and  FAT$W_FFBYTE  will  contain  512,  or  FAT$L_EFBLK  may
          contain  n+1 and FAT$W_FFBYTE will contain 0.  The preferred
          method is to set FAT$W_FFBYTE to zero.



6.1.7  FAT$B_BKTSIZE - 1 Byte           File Bucket Size

          This  byte  contains  the  number  of  virtual  blocks  that
          constitute   one  storage  bucket  for  non-sequential  file
          formats.  It is not used for sequential file formats.



6.1.8  FAT$B_VFCSIZE - 1 Byte           Fixed Control Area Size

          This byte contains the number of bytes at the start of  each
          variable  length  record  that constitute the record's fixed
          control area.



6.1.9  FAT$W_MAXREC - 2 Bytes           Maximum Record Size

          This word contains the maximum  size  in  bytes  of  records
          permitted  in  the file.  For fixed length record files, the
          contents of FAT$W_MAXREC and FAT$W_RSIZE are equal.



6.1.10  FAT$W_DEFEXT - 2 Bytes          Default Extend Size

          This field specifies the number of blocks by which to extend
          the  file when more space is needed, and no extend quantitiy
          has been supplied by the application.

Files-11 On-Disk Structure                                     Page 60


6.1.11  FAT$W_GBC - 2 Bytes             Global Buffer Count

          This word specifies the number of buffers to be allocated to
          a global buffer pool for managing the file, if not specified
          by the application.



6.1.12  8 Bytes                         (Not used)

6.1.13  FAT$W_VERSIONS - 2 Bytes        Directory   Default    Version
        Limit

          This word is  only  used  in  the  record  attributes  of  a
          directory  file.   It  specifies  the  version  limit  to be
          assigned to new files  created  in  the  directory  when  no
          version  limit  is siven by the user.  A value of zero means
          the version limit is set to 32767, the maximum possible.



6.1.14  FAT$C_LENGTH - 32 Bytes         Size of Attribute Block


          This symbol represents the total number of bytes in the file
          attribute block.



6.2  File Attributes Layout

                |-------------------|-------------------|
FAT$B_RATTRIB   |   Record Attr.    |    Record Type    |   FAT$B_RTYPE
                |-------------------|-------------------|
                |          Record Size (Bytes)          |   FAT$W_RSIZE
                |---------------------------------------|
                |              Highest VBN              |   FAT$L_HIBLK
                |--                                   --|
                |               Allocated               |    
                |---------------------------------------|
                |              End of File              |   FAT$L_EFBLK
                |--                                   --|
                |                  VBN                  |    
                |---------------------------------------|
                |            First Free Byte            |   FAT$W_FFBYTE
                |-------------------|-------------------|
FAT$B_VFCSIZE   | Fixed Ctrl. Size  |    Bucket Size    |   FAT$B_BKTSIZE
                |-------------------|-------------------|
                |          Maximum Record Size          |   FAT$W_MAXREC
                |---------------------------------------|
                |          Default Extend Size          |   FAT$W_DEFEXT
                |---------------------------------------|
                |          Global Buffer Count          |   FAT$W_GBC
                |---------------------------------------|
                |                                       |

Files-11 On-Disk Structure                                     Page 61


                |                                       |
                |                                       |
                |               (Not used)              |
                |                                       |
                |                                       |
                |                                       |
                |---------------------------------------|
                |    Directory Default Version Limit    |   FAT$W_VERSIONS
                |---------------------------------------|   FAT$C_LENGTH



6.3  Attribute Standardization

To assure a certain consistency of  file  record  structures,  certain
fields  in  the  record  attributes  area  are  standardized, and must
contain well defined values regardless of the record structure or file
organization in use.

     1.  The record type byte (FAT$B_RTYPE) must contain a  code  that
         identifies  the  file organization and record structure.  All
         codes must be registered with this specification.

     2.  The record attribute bits should be used as  described  above
         when  applicable.   New  attributes ahould be registered with
         this specification.

     3.  The high VBN field (FAT$L_HIBLK) must contain the  number  of
         blocks  allocated  to the file.  File systems may modify this
         field during some operations on the file.

     4.  The end of file mark (FAT$L_EFBLK  and  FAT$W_FFBYTE)  should
         describe the end of data in the file when applicable.




6.4  Record Structure

This section describes how records are packed in the virtual blocks of
a disk file.  In general, a file is treated as a sequentially numbered
array of bytes.  Records are numbered consecutively starting with 1.



6.4.1  Fixed Length Records

In a file consisting of fixed length records, the records  are  simply
packed  end  to  end  with  no additional control information.  If the
record length is odd, each record is padded with a single  null.   For
direct access, the address of a record is computed as follows:

Let:      n = record number
          k = record size (in bytes)
          m = byte address of record in file

Files-11 On-Disk Structure                                     Page 62


          q = number of records per block
          j = VBN containing the start of the record
          i = byte offset within VBN j

Then      h = ((k+1)/2)*2 (rounded up record length)
          m = (n-1)*h
          j = m/512+1 (truncated)
          i = m mod 512

          Note that m is potentially as large as 41 bits (unsigned).

The previous discussion assumes that records  cross  block  boundaries
(that  is,  FAT$V_NOSPAN  is  not set).  If records do not cross block
boundaries, they are limited to 512 bytes, and the following equations
apply (the variables are defined as above):

          h = ((k+1)/2)*2 (rounded up record length)
          q = 512/h (truncated)
          j = (n-1)/q+1 (truncated)
          i = ((n-1) mod q)*h



6.4.2  Variable Length Records

In a sequential file consisting of variable  length  records,  records
may  be up to 32767 bytes in length.  Each record is preceded by a two
byte binary count of the bytes in  the  record  (the  count  does  not
include  itself).   For  example,  a  null  record is represented by a
single zero word.  The byte count is always word aligned; i.e.,  if  a
record ends on an odd byte boundary, it is padded with a single null.

If records do not cross block boundaries (FAT$V_NOSPAN is  set),  they
are  limited  to a size of 510 bytes.  A byte count of -1 is used as a
flag to signal that there are no more records in a  particular  block.
The  remainder of that block is then dead space and the next record in
the file starts at the beginning of the next block.  The contents of a
block after the end marker are undefined.



6.4.3  Variable Length Records with Fixed Control Area

The format of a VFC file is identical to a variable length record file
except  that  a  fixed control area field is located immediately after
the byte count field of each record.   This  field  may  be  used  for
various  purposes by different applications.  For example, editors may
use it to store line numbers, or it may hold  an  audit  tag  for  the
record,  etc.   The  control  area is not returned as part of the data
when a record is read, but is available  separately.   Note  that  the
record  byte  count field counts the fixed control area as well as the
data of the record.

Files-11 On-Disk Structure                                     Page 63


6.4.3.1  Format of Two Byte Print Control Field in FAT$C_VFC Records

If the FAT$V_PRINTCC bit is set in the record attributes  then  a  two
byte  control  area  is  used to contain carriage control data for the
record.  Byte 0 is print control information to act  upon  before  the
record data is output to a unit record device; byte 1 is print control
information to act upon after the record data has  been  output  to  a
unit record device.

The format of each byte is as follows:

Bit 7       Bits 6-0     Meaning

0           0            No carriage control
0           count(1-127) "count" new lines (CR/LF)

Bit 7       Bit 6  Bit 5  Bits 4-0       Meaning

1           0      0      ASCII C0 set   ASCII char to
                                         output (CR,FF etc.)
1           0      1      ASCII C1 set   ASCII char (8 bit code)
                                         to output
1           1      0      code (0-63)    Device specific code
1           1      1      -              Reserved



6.4.4  Stream Format Records

In a stream format file, the data bytes  of  the  records  are  simply
packed  into  consecutive bytes of the file's virtual blocks.  Certain
characters  are  interpreted  as  record  terminators;  the   set   of
terminators varies with the different stream formats.

The carriage control attributes play  a  somewhat  different  role  in
stream  format  files  than  they  do  in record files.  When a stream
format file is  read  or  written,  the  carriage  control  attributes
determine  whether  the  record terminator character is visible to the
application processing the file.  Each stream format has some  set  of
terminator  characters  or  character  sequences.   Of  these,  one is
                   _______ __________referred to as the default terminator; it is considered the  principal
terminator for that file format.

Of  the  three  carriage  control  attributes,   FAT$V_FORTRANCC   and
FAT$V_IMPLIEDCC  are legal for stream files; FAT$V_PRINTCC is not.  If
either of the two legal carriage control attributes  is  set  for  the
file, then terminators receive the following treatment:

On input,  if  the  record  ends  with  the  default  terminator,  the
terminator  is not presented to the application as part of the record.
If the record ends with a terminator other than the default, than  the
terminator is considered part of the record.

Conversely, on output, if the record presented for output does not end
with  a  recognized  terminator, the default terminator is appended to

Files-11 On-Disk Structure                                     Page 64


the record; if  the  record  does  end  with  a  terminator,  then  no
terminator is appended.

If no carriage control is set  for  the  file,  then  terminators  are
always  considered  part of the record on input, and none are added on
output.

The following sections describe the terminator sets  for  the  various
stream formats.



6.4.4.1  Undefined Records (Binary Stream)

No characters are considered terminators.  When such a file  is  read,
the  application  always receives the number of bytes specified as the
size of its input record buffer.  The carriage control attributes  are
irrelevant for this file format.



6.4.4.2  General Stream Format

The terminator set includes the sequence carriage return - line  feed,
and  the  characters  carriage  return,  line feed, vertical tab, form
feed, and escape.  The default terminator  is  the  sequence  carriage
return  - line feed.  This is the format used by the stream support in
most DEC operating systems.



6.4.4.3  Line Feed Stream Format

Line feed is the only and default terminator.  This is the format used
in UNIX text files.



6.4.4.4  Carriage Return Stream Format

Carriage return is the only  and  default  terminator.   This  is  the
format  used in APL text files, and the text file format of some other
manufacturers' operating systems.



7  Simple Subset

This section describes a minimal subset of Files-11 structure level  2
which  is  suitable  for data interchange and be read on small systems
with a minimum of software.  The subset is referred to as the Files-11
level 0 subset.  The subset is achieved by the omission of a number of
Files-11's features and a set of format rules that  allow  simplifying
assumptions to be made by the software reading the volume.

Files-11 On-Disk Structure                                     Page 65


Level 0 has been designed so that it  can  be  produced  by  a  fairly
conventional  file  system,  using  restricted operation.  It contains
sufficient flexibility, however, that it may  also  be  produced  with
unconventional  storage  allocation  techniques  (i.e.,  using special
purpose software that itself incorporates simplifying assumptions).

Storage management facilities  are  optional;  further,  some  of  the
format rules preclude dynamic storage allocation.  Because the primary
use is in data interchange, all ownership and protection features  are
likewise  absent.   Disks containing level 0 structures are assumed to
be good.  Further, the software reading them may assume that the  file
structure is correct, once having validated the structure level.  This
eliminates all of the consistency  checks  normally  present  in  full
Files-11 implementations, at a considerable savings in code size.

Notwithstanding the simplifications, level 0 Files-11 disks are  still
completely valid Files-11 structures, and can be read by full Files-11
implementations with all consistency checks enforced.

Subset level 0 is identified by a structure level value  in  the  home
block  and file header of 514 (representing a structure level of 2 and
a structure version of 2).  The following  structural  simplifications
are made in the level 0 subset:

     1.  No  multi-header  files  (except  to  represent  multi-volume
         files)

     2.  Contiguous files only (except the index file)

     3.  Only one version per file

     4.  The index file consists of two contiguous parts.

     5.  Only two reserved files are actually used:   The  index  file
         and the MFD.  All other reserved headers are optional.

     6.  The header and ident areas of the file header  are  of  fixed
         length, so that the ident and map area may be dead-reckoned.

     7.  The map area  contains  exactly  one  format  3  map  pointer
         (except for the index file).

     8.  There is one file record format  for  text  files  meant  for
         gerenal  interchange:   general  stream  format.   Other file
         formats may be present at the option of the user.

     9.  Once the format has been identified as subset  level  0  from
         the structure level in the home block, the implementation may
         assume that the file structure is valid and is not obliged to
         do  consistency checking.  Checking the checksums of the home
         block is optional.

Use of level 0 (by its recipient, not the system  creating  the  disk)
implies the following functional restrictions:

Files-11 On-Disk Structure                                     Page 66


     1.  Access to the disk is read-only.

     2.  No protection or accounting features

     3.  Only one version per file

     4.  Only two reserved files are actually used:   The  index  file
         and the MFD.  All other reserved headers are optional.

     5.  Only general stream files are required  by  level  0.   Other
         file record formats are optional.

The following pictures give the detailed breakdown of the contents and
use  of  fields  in  the  various Files-11 structures.  The fields are
identified by symbolic field name only; for further explanation, refer
to  the  main  body of this specification.  The contents of the fields
are identified as follows:

Zero             The field is not used in the level 0 subset and  must
                 contain zero.

Ignored          The field is not used in the level 0 subset.  It  may
                 contain  zero  or  its normal value as defined by the
                 main body of this specification.

(numeric value)  The field always contains the specified value.

Valid            The field contains its normal value as defined by the
                 main  body  of this specification, but is not used or
                 verified by the level 0 implementation.

Valid, used      The field contains its normal value as defined by the
                 main  body  of  this  specification,  and  is used or
                 verified by the level 0 implementation.



7.1  File ID Layout, Level 0 Subset

                |---------------------------------------|
                |              Valid, used              |  FID$W_NUM
                |---------------------------------------|
                |                 Valid                 |  FID$W_SEQ
                |-------------------|-------------------|
FID$B_NMX       |    Valid, used    |    Valid, used    |  FID$B_RVN
                |-------------------|-------------------|



7.2  Index File Structure

The index file of a level 0 disk has the same format and structure  as
a  normal  index  file,  as  described in section 5.1.8.  However, its
placement is constrained.  The index file  consists  of  two  extents.
The  first extent contains clusters 1 through 4 (i.e., the boot block,

Files-11 On-Disk Structure                                     Page 67


home blocks, and backup index file header), and is located starting at
LBN  0.   The  second extent of the index file contains the index file
bitmap and all file headers, and may be located anywhere on the disk.



7.3  File Header Layout, Level 0 Subset

Header Area

                |-------------------|-------------------|
FH2$B_MPOFFSET  |        104        |        44         |   FH2$B_IDOFFSET
                |-------------------|-------------------|
FH2$B_RSOFFSET  |        255        |        255        |   FH2$B_ACOFFSET
                |-------------------|-------------------|
                |                 Valid                 |   FH2$W_SEG_NUM
                |---------------------------------------|
                |                  514                  |   FH2$W_STRUCLEV
                |---------------------------------------|   FH2$W_FID
                |                                       |   FH2$W_FID_NUM
                |--                                   --|
                |                 Valid                 |   FH2$W_FID_SEQ
                |--                                   --|
FH2$B_FID_NMX   |                                       |   FH2$B_FID_RVN
                |---------------------------------------|   FH2$W_EXT_FID
                |                                       |   FH2$W_EX_FIDNUM
                |--                                   --|
                |              Valid, used              |   FH2$W_EX_FIDSEQ
                |--                                   --|
FH2$B_EX_FIDNMX |                                       |   FH2$B_EX_FIDRVN
                |---------------------------------------|
                |                                       |   FH2$W_RECATTR
                |                                       |
                |                                       |
                |              Valid, used              |    
                |                                       |
                |                                       |
                |                                       |
                |---------------------------------------|
                |                                       |   FH2$L_FILECHAR
                |--               Valid               --|
                |                                       |
                |---------------------------------------|
                |                Ignored                |   FH2$W_RECPROT
                |-------------------|-------------------|
FH2$B_ACC_MODE  |      Ignored      |         4         |   FH2$B_MAP_INUSE
                |-------------------|-------------------|
                |                                       |   FH2$L_FILEOWNER
                |--              Ignored              --|
                |                                       |
                |---------------------------------------|
                |                Ignored                |   FH2$W_FILEPROT
                |---------------------------------------|   FH2$W_BACKLINK
                |                                       |   FH2$W_BK_FIDNUM
                |--                                   --|

Files-11 On-Disk Structure                                     Page 68


                |                 Valid                 |   FH2$W_BK_FIDSEQ
                |--                                   --|
FH2$B_BK_FIDNMX |                                       |   FH2$B_BK_FIDRVN
                |---------------------------------------|
                |                Ignored                |   FH2$W_JOURNAL
                |---------------------------------------|
                |              (not used)               |
                |---------------------------------------|
                |                                       |   FH2$L_HIGHWATER
                |--               Valid               --|
                |                                       |
                |---------------------------------------|
                |                                       |
                |--                                   --|
                |                                       |
                |--            (not used)             --|
                |                                       |
                |--                                   --|
                |                                       |
                |---------------------------------------|


Ident Area

                |---------------------------------------|
                |                                       |   FI2$T_FILENAME
                |--                                   --|
                |                                       |
                |--                                   --|
                |                 Valid                 |    
                |--                                   --|
                |                                       |
                |--                                   --|
                |                                       |
                |---------------------------------------|
                |                 Valid                 |   FI2$W_REVISION
                |---------------------------------------|
                |                                       |   FI2$Q_CREDATE
                |--                                   --|
                |                                       |
                |--               Valid               --|
                |                                       |
                |--                                   --|
                |                                       |
                |---------------------------------------|
                |                                       |   FI2$Q_REVDATE
                |--                                   --|
                |                                       |
                |--               Valid               --|
                |                                       |
                |--                                   --|
                |                                       |
                |---------------------------------------|
                |                                       |   FI2$Q_EXPDATE
                |--                                   --|

Files-11 On-Disk Structure                                     Page 69


                |                                       |
                |--               Valid               --|
                |                                       |
                |--                                   --|
                |                                       |
                |---------------------------------------|   
                |                                       |   FI2$Q_BAKDATE
                |--                                   --|
                |                                       |
                |--              Ignored              --|
                |                                       |
                |--                                   --|
                |                                       |
                |---------------------------------------|
                |                                       |   FI2$T_FILENAMEXT
                |                                       |
                |                                       |
                |                 Valid                 |
                |                                       |
                |                                       |
                |                                       |
                |---------------------------------------|   FI2$C_LENGTH



Map, ACL, and Reserved Areas

                |----|----------------------------------|
FM2$V_FORMAT    | 11 |          Valid, used             |  FM2$V_COUNT2
                |----|----------------------------------|
                |              Valid, used              |  FM2$W_LOWCOUNT
                |---------------------------------------|
                |                                       |  FM2$L_LBN3
                |--            Valid, used            --|
                |                                       |
                |---------------------------------------|
                |                                       |
                |                                       |
                |                 Zero                  |
                |                                       |
                |                                       |
                |---------------------------------------|
                |                 Valid                 |   FH2$W_CHECKSUM
                |---------------------------------------|


Note that the access control list and reserved areas are null.



7.4  Directory Record Layout, Level 0 Subset

                |---------------------------------------|
                |              Valid, used              |   DIR$W_SIZE
                |---------------------------------------|

Files-11 On-Disk Structure                                     Page 70


                |                Ignored                |
                |-------------------|-------------------|
DIR$B_NAMECOUNT |    Valid, used    |         0         |   DIR$B_FLAGS
                |-------------------|-------------------|
                |                                       |   DIR$T_NAME
                |                                       |
                |                                       |
                |              Valid, used              |
                |                                       |
                |                                       |
                |                                       |
                |---------------------------------------|
                |              Valid, used              |   DIR$W_VERSION
                |---------------------------------------|   DIR$W_FID
                |                                       |   DIR$W_FID_NUM
                |--                                   --|
                |              Valid, used              |   DIR$W_FID_SEQ
                |--                                   --|
DIR$B_FID_NMX   |                                       |   DIR$B_FID_RVN
                |---------------------------------------|



7.5  Home Block Layout, Level 0 Subset

                |---------------------------------------|
                |                                       |   HM2$L_HOMELBN
                |--               Valid               --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$L_ALHOMELBN
                |--                 2                 --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$L_ALTIDXLBN
                |--                 3                 --|
                |                                       |    
                |---------------------------------------|
                |                  513                  |   HM2$W_STRUCLEV
                |---------------------------------------|
                |                 Valid                 |   HM2$W_CLUSTER
                |---------------------------------------|
                |                 Valid                 |   HM2$W_HOMEVBN
                |---------------------------------------|
                |                 Valid                 |   HM2$W_ALHOMEVBN
                |---------------------------------------|
                |                 Valid                 |   HM2$W_ALTIDXVBN
                |---------------------------------------|
                |                 Valid                 |   HM2$W_IBMAPVBN
                |---------------------------------------|
                |                                       |   HM2$L_IBMAPLBN
                |--            Valid, used            --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$L_MAXFILES

Files-11 On-Disk Structure                                     Page 71


                |--               Valid               --|
                |                                       |   
                |---------------------------------------|
                |              Valid, used              |   HM2$W_IBMAPSIZE
                |---------------------------------------|
                |                 Valid                 |   HM2$W_RESFILES
                |---------------------------------------|
                |                Ignored                |   HM2$W_DEVTYPE
                |---------------------------------------|
                |              Valid, used              |   HM2$W_RVN
                |---------------------------------------|
                |              Valid, used              |   HM2$W_SETCOUNT
                |---------------------------------------|
                |                Ignored                |   HM2$W_VOLCHAR
                |---------------------------------------|
                |                                       |   HM2$L_VOLOWNER
                |--              Ignored              --|
                |                                       |   
                |---------------------------------------|
                |                                       |
                |--            (not used)             --|
                |                                       |   
                |---------------------------------------|
                |                Ignored                |   HM2$W_PROTECT
                |---------------------------------------|
                |                Ignored                |   HM2$W_FILEPROT
                |---------------------------------------|
                |              (not used)               |
                |---------------------------------------|
                |                 Valid                 |   HM2$W_CHECKSUM1
                |---------------------------------------|
                |                                       |   HM2$Q_CREDATE
                |--                                   --|
                |                                       |   
                |--               Valid               --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |-------------------|-------------------|
HM2$B_LRU_LIM   |      Ignored      |      Ignored      |   HM2$B_WINDOW
                |-------------------|-------------------|
                |                Ignored                |   HM2$W_EXTEND
                |---------------------------------------|
                |                                       |   HM2$Q_RETAINMIN
                |--                                   --|
                |                                       |   
                |--              Ignored              --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$Q_RETAINMAX
                |--                                   --|
                |                                       |   
                |--              Ignored              --|

Files-11 On-Disk Structure                                     Page 72


                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$Q_REVDATE
                |--                                   --|
                |                                       |   
                |--              Ignored              --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$R_MIN_CLASS
                |--                                   --|
                |                                       |   
                |--                                   --|
                |                Ignored                |   
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$R_MAX_CLASS
                |--                                   --|
                |                                       |   
                |--                                   --|
                |                Ignored                |   
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |                                       |    
                |                                       |    
                |                                       |    
                |                                       |    
                |              (not used)               |
                |                                       |    
                |                                       |    
                |                                       |    
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$L_SERIALNUM
                |--              Ignored              --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$T_STRUCNAME
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |--               Valid               --|
                |                                       |    
                |--                                   --|
                |                                       |    

Files-11 On-Disk Structure                                     Page 73


                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$T_VOLNAME
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |--               Valid               --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$T_OWNERNAME
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |--               Valid               --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |                                       |   HM2$T_FORMAT
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |--            FILES11B_L0            --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |--                                   --|
                |                                       |    
                |---------------------------------------|
                |              (not used)               |
                |---------------------------------------|
                |                 Valid                 |   HM2$W_CHECKSUM2
                |---------------------------------------|



7.6  File Attributes Layout, Level 0 Subset

                |-------------------|-------------------|
FAT$B_RATTRIB   |       Valid       |    Valid, used    |   FAT$B_RTYPE
                |-------------------|-------------------|
                |                 Valid                 |   FAT$W_RSIZE
                |---------------------------------------|
                |                                       |   FAT$L_HIBLK
                |--               Valid               --|

Files-11 On-Disk Structure                                     Page 74


                |                                       |    
                |---------------------------------------|
                |                                       |   FAT$L_EFBLK
                |--            Valid, used            --|
                |                                       |    
                |---------------------------------------|
                |--            Valid, used            --|   FAT$W_FFBYTE
                |-------------------|-------------------|
FAT$B_VFCSIZE   |       Valid       |       Valid       |   FAT$B_BKTSIZE
                |-------------------|-------------------|
                |                 Valid                 |   FAT$W_MAXREC
                |---------------------------------------|
                |                 Valid                 |   FAT$W_DEFEXT
                |---------------------------------------|
                |                 Valid                 |   FAT$W_GBC
                |---------------------------------------|
                |                                       |
                |                                       |
                |                                       |
                |               (Not used)              |
                |                                       |
                |                                       |
                |                                       |
                |---------------------------------------|
                |                Ignored                |   FAT$W_VERSIONS
                |---------------------------------------|   FAT$C_LENGTH



[End of ODS2.RNO]